## Slide 1: Guidance on MPE scenario
AI. 9.4.1
Document for: Discussion
RP-191492

## Slide 2: Background – RAN1#97 Agreement
Down-select in RAN1#98 from the following options for beam management enhancements:
Alt1. Support UE to report CRI/SSBRI where the CRI/SSBRI refers to a preferred spatial relation RS for UL transmission
  FFS: Whether to support SRI in addition to CRI/SSBRI
  FFS on details of the reporting configuration (e.g. separate or joint reporting with existing DL beam reporting, introduction of new information from UE such as MPR)
Alt2. Support SRI field in the DCI can be used to indicate multiple SRS resources and UE’s autonomous selection of one SRS resource for PUSCH beam determination out of the multiple
Alt3: Reuse Rel-15 beam specific PHR reporting to determine beam-specific MPE impact transparently, i.e., by difference value between Pc,max (which is calculated based on P-MPR) and the required transmission power.
  FFS: Enhancement on UL beam configuration for virtual PHR.
Alt4: No enhancements considering MPE issues in Rel-16 RAN1 specifications. It is up to UE implementation in conjunction to RAN4 specification support.
If no consensus in RAN1#98, no further discussion in RAN1.

## Slide 3: Background – RAN#84 discussion
It is understood that Alt4 is what Rel-15 UEs already do
Alt4 is not an option for Rel-16
  Alt4: No enhancements considering MPE issues in Rel-16 RAN1 specifications. It is up to UE implementation in conjunction to RAN4 specification support.

## Slide 4: Proposal
Add the following bullet to the eMIMO WID:
  Specify air interface solution targeting MPE issue for UL transmissions in FR2 enabling UL transmissions at higher duty cycle and/or power level than it would be possible with Rel-15 based solutions, while having no impact on DL operation