## Slide 1: Agenda Item : 9.4.1 Source : Samsung Title : Clarification on MPE issue per NR_eMIMO Work Item Document for : Discussion
3GPP TSG RAN meeting #84 RP-191562
Newport Beach, USA, June 3-7, 2019

## Slide 2: Background
The work on multi-beam in Rel.16 WID is as follows:
  Enhancements on multi-beam operation, primarily targeting FR2 operation:
    [MB1a] Perform study and, if needed, specify enhancement(s) on UL and/or DL transmit beam selection specified in Rel-15 to reduce latency and overhead
    [MB1b] Specify UL transmit beam selection for multi-panel operation that facilitates panel-specific beam selection
    [MB2a] Specify a beam failure recovery for SCell with DL/UL as well as DL-only, where PCell can be operating in FR1 as well as FR2 based on the beam failure recovery specified in Rel-15
    [MB2b] Specify measurement and reporting of either L1-RSRQ or L1-SINR
The following was agreed in RAN1#97 (Reno):
  Down-select in RAN1#98 from the following options for beam management enhancements:
    Alt1. Support UE to report CRI/SSBRI where the CRI/SSBRI refers to a preferred spatial relation RS for UL transmission
      …
    Alt2. Support SRI field in the DCI can be used to indicate multiple SRS resources and UE’s autonomous selection of one SRS resource for PUSCH beam determination out of the multiple
    Alt3: Reuse Rel-15 beam specific PHR reporting to determine beam-specific MPE impact transparently, i.e., by difference value between Pc,max (which is calculated based on P-MPR) and the required transmission power.
      …
    Alt4: No enhancements considering MPE issues in Rel-16 RAN1 specifications. It is up to UE implementation in conjunction to RAN4 specicfiation support.
  If no consensus in RAN1#98, no further discussion in RAN1.
RAN1 is currently performing study on a number of proposals for reducing latency/overhead of TX beam selection
  One category (studied under MB1a) is the MPE issue, to be finalized in RAN1#98

## Slide 3: Current status in RAN1 (up to RAN1#97)
In RAN1, 4 alternatives have been proposed and identified to address the MPE issue
  2 alternatives on new signaling (Alt1 and Alt2)
  2 alternatives on using the existing Rel.15 feature(s) implying that there is no need for Rel.16 PHY-layer (RAN1 spec) enhancement (Alt3 and Alt4)
RAN4 LS on MPE (first presented in RAN1 @RAN1#96bis) has solicited responses in RAN1 (RAN1#96bis and 97)
  E.g. one set of results was presented, demonstrating no benefit for Alt1 and Alt2 (cf. Ericsson’s R1-1907436 and R1-1907476) in mitigating UL coverage impact of MPE
  @RAN1#97, it was agreed to give more time to study this issue until RAN1#98
Therefore, the WID modification proposal in RP-191492 deviated from the agreement @RAN1#97 and would circumvent
  The due process/procedure in RAN1, and
  The need for “performing study before deciding whether or not to specify” Alt1 and/or Alt2 for MPE issue

## Slide 4: Assessment on claim/proposal in RP-191492
RP-191492 claims that Alt4 amounts to “do(ing) nothing” therefore “is not an option for Rel-16”
  “Specify(ing) air interface solution targeting MPE issue for UL transmissions in FR2 enabling UL transmissions at higher duty cycle and/or power level than it would be possible with Rel-15 based solutions, while having no impact on DL operation” is in the scope of Rel.16 NR_eMIMO WI
  Therefore Alt4 amounts to RAN1 down scoping without further agreement
Assessment: the above claim is incorrect
  WID: [MB1a] “Perform study and, if needed, specify enhancement(s) on UL and/or DL transmit beam selection specified in Rel-15 to reduce latency and overhead”
  “Specify(ing) air interface solution targeting MPE issue for UL transmissions …” may not be within the WI scope
  But “performing study and, if needed, specifying air interface solution targeting MPE …” could be considered under MB1a and hence is within the WI scope
  Thus, RAN1 follows the WID ‘down to the letter’ while the proposal in RP-191492 seeks to modify the WID by circumventing the due process/procedure in RAN1
    Alt4 could be the outcome if Alt1/Alt2 demonstrates no benefit for mitigating the MPE issue

## Slide 5: Conclusion
Pertaining to MPE issue, down selection on 4 alternatives until RAN1#98 (Prague, August 2019) is in line with Rel.16 NR_eMIMO WI scope and proper working procedure:
  Perform study and, if needed, specify enhancement(s) on UL and/or DL transmit beam selection specified in Rel-15 to reduce latency and overhead
  Per agreement in RAN1#97:
    Down-select in RAN1#98 from the following options for beam management enhancements:
      Alt1. Support UE to report CRI/SSBRI where the CRI/SSBRI refers to a preferred spatial relation RS for UL transmission
        …
      Alt2. Support SRI field in the DCI can be used to indicate multiple SRS resources and UE’s autonomous selection of one SRS resource for PUSCH beam determination out of the multiple
      Alt3: Reuse Rel-15 beam specific PHR reporting to determine beam-specific MPE impact transparently, i.e., by difference value between Pc,max (which is calculated based on P-MPR) and the required transmission power.
        …
      Alt4: No enhancements considering MPE issues in Rel-16 RAN1 specifications. It is up to UE implementation in conjunction to RAN4 specicfiation support.
    If no consensus in RAN1#98, no further discussion in RAN1.
No need to modify Rel.16 NR_eMIMO WID in RAN#84