## Slide 1: Motivation for Study on RAN-Centric Data Collection and Utilization Enhancement
CMCC
3GPP TSG RAN Meeting #85 RP-191785
Newport Beach, USA, September 16-20, 2019
Document for: discussion
Agenda Item: 8.1.12

## Slide 2: Progress of R16 RAN-centric DCU (801000)
Basic SON/MDT functions have been studied
  CCO, PCI Selection, MRO, MLB, RACH optimization, Energy Saving, MDT
Initial consideration on NR features
  CU-DU split, MR-DC, inactive, beamforming, …
Leftover use cases due to time limitation
  Massive MIMO
  System Information Transmission optimization
  RAN Notification Area Optimization
  Edge Computing Optimisation
  Per-UE Local RRM Policy Information Storage and Retrieval
  …

## Slide 3: Study on RAN-Centric DCU Enhancement is necessary
Leftover use cases of Rel-16 RCU
Further enhancements of SON/MDT for NR, including the consideration of R16 new features, e.g. NR-U, NR V2X
  Improvement of ANR, MRO, MLB, RACH optimization, Energy Saving, etc
  Improvement of MDT, including Logged MDT and immediate MDT, signalling-based and management-based MDT
Identify new use cases and potential architecture and protocol impacts
  QoE enhancement
  Log behaviour mismatch between UE expectation and network action
  RAN data collection as input of Machine Learning & Artificial Intelligence

## Slide 4: Leftovers – RAN Notification Area Optimization
As long as the RRC_inactive UE is moving towards cells which are part of the configured RNA, it does not have to notify NG-RAN
When it moves towards a cell which is not part of the configured RNA, then it has to send an RNA update (RNAU)
The design of the RNA has impact on the overhead produced by RNAUs or paging
  Small RNAs will cause a lot of RNAUs
  Large RNAs will cause a lot of paging overhead

## Slide 5: Leftovers – System Information Transmission optimization
SIBs other than SIB1 are delivered to the UE via SI messages
  Each SI message consists of SIBs having the same periodicity.
  Indication of whether an Other SI message is broadcasted or not is given in SIB1
Further study on SI Area planning and transmission of SIBs, e.g. broadcasting or on-demand
Any SIB except SIB1 can be configured to be cell specific or area specific using an indication in SIB1
Cell specific SIB is applicable only within a cell
Area specific SIB is applicable within an area referred to as SI area

## Slide 6: New use case - QoE Enhancement
Understanding customers’ experience, e.g. throughput, data loss, latency, is beneficial for operators
QoE measurement can be defined based on different Vertical Applications and measurement takes place at UE’s application layer
  streaming services evaluation standard was defined by ITU
  how to evaluate Dynamic Adaptive Streaming over HTTP was defined in SA4
  SA5 has studied the management solution for collection of QoE information and proposed use cases, potential requirements and possible solutions
Based on the work above, the operators can collect and utilize the QoE measurement information in order to monitor the user experience and optimize NW

## Slide 7: New use case – Behaviour mismatch between UE expectation & network action
The overheating issue and suggested configuration is reported from UE, but no response received or the response from NW side cannot relieve it effectively
Event-based measurements are reported by UE, but no handover command received

## Slide 8: Thank You Q&A