## Slide 1: Views on Multi-SIM device in Rel-17 RAN and SA
vivo
RP-191897
3GPP TSG-RAN WG Meeting #85
Newport Beach, USA, Sep 16th-20th, 2019
Agenda Item: 8.1.3

## Slide 2: Background
SA2 has set up a study on system enablers for multi-SIM devices in SP-190248
Multi-SIM has also been identified as one RAN working area for Rel-17 in RAN#84
  An email discussion was assigned to identify the RAN impact of target use cases
    Case1: Collision between Paging reception from network A and B
    Case2: Paging delivery to UE on network A while the UE is actively communicating (i.e. RRC connected mode) with network B
    Case3: UE entering in RRC Connected mode in network A from Idle/Inactive mode, while UE is already in RRC Connected mode in network B
    Case4: UE communicates with network A and B simultaneously
    Case5: Interference between different USIMs including dual Tx/ dual Rx and single TX/dual Rx

## Slide 3: Use cases in RAN and SA
Potential RAN Scope | SA SID | Potential SA requirement
Case1: Collision between Paging reception from network A and B | A mechanism for avoidance of paging collisions occurring in the UE between USIM A and USIM B | Overlap，CN Solution was mentioned during email discussion. Some companies would like to wait SA progress firstly. SA should coordinate with RAN to ensure the paging can be delivered in Uu with low missing rate.
Case2: Paging delivery to UE on network A while the UE is a | A mechanism for delivering paging destined to USIM A while the UE is actively communicating with USIM B | Overlap, additional information in paging message, e.g., paging case in idle and inactive state. CN inputs are needed.
Case3: UE entering in RRC Connected mode in network A from Idle/Inactive mode, while UE is already in RRC Connected mode in network B | A mechanism allowing for suspension (or release) and resumption of an ongoing connection in the 3GPP system associated with USIM A, so that the UE can temporarily leave to the 3GPP system associated with USIM B, and then return to the 3GPP system in a network-controlled manner. The study shall determine how the network handles MT data or MT control-plane activity occurrence on a suspended connection. | Overlap, RAN or CN is responsible to release the existing connection SA should coordinate with RAN to make a decision.
Case4: UE communicates with network A and B simultaneously | Handling of emergency calls and sessions | Independent case with SA, No SA requirements
Case5: Interference between different USIMs including dual Tx/ dual Rx and single TX/dual Rx | Handling of service prioritization i.e. the study shall determine whether the UE behaviour upon reception of paging information is driven by USIM configuration or user preferences or both | Independent case with SA, No SA requirements

## Slide 4: Network operation and UE types
Potential RAN scope | SA | Comparison
Inter-MNO and intra-MNO | Inter-MNO and intra-MNO | Same
a) single RX, single Tx b) dual Rx, single Tx c) dual Rx, dual Tx | a) single RX, single Tx b) dual Rx, single Tx | One more UE type in RAN
LTE only +NR SA NR SA + NR SA LTE only +EN-DC EN-DC + NR SA | LTE and NR | DC case have more RAN impacts

## Slide 5: SA observations and requirement
There are three use cases and two UE types which are overlapping between RAN and SA
RAN impacts for both overlapping use cases and independent use case have been identified during email discussion.
Early progress for overlapping use cases in SA are helpful for RAN Multi-SIM work