## Slide 1
Views on Further enhanced NR UE power saving in Rel-17
3GPP TSG RAN Meeting #85 RP-191901
Newport Beach, USA, September 16-20, 2019
Agenda item: 8.1.8
Notes: 1st,

## Slide 2: UE power saving features in Rel-15/16
Basic UE power saving features provided in Rel-15
  Bandwidth part adaptation
  DRX
  RRC_INACTIVE state
  Configurable PDCCH monitoring periodicity
Enhanced UE power saving features provided in Rel-16
  UE adaptation in RRC_CONNECTED state
    Basic WUS function: Wake-up PDCCH to trigger UE activity for the next DRX ON cycle
    Adaptation between same-slot and cross-slot scheduling
    UE adaptation to the maximum MIMO layer
    UE assistant information for state transition and DRX parameters
    Scell “dormancy” through dynamic PDCCH monitoring adaptation (MR-DC/CA)
  RRM relaxation for neighbour cells in RRC_IDLE/INACTIVE state

## Slide 3: Further enhanced UE power saving features in Rel-17
Further enhanced UE power saving should be considered in Rel-17 for different RRC states
  Enhancements to RRC_CONNECTED state is beneficial for all UE types (smartphone, wearable )
  Enhancements to RRC_IDLE/INACTIVE state is especially beneficial for wearable devices
Further power saving enhancements for RRC_CONNECTED state
  Enhanced WUS function to indicate UE adaptation for the next DRX on cycle, for example maximum MIMO layer, BWP, Scell (if not addressed in Rel-16)
  PDCCH monitoring reduction during DRX active time (if not addressed in Rel-16)
  RLM/BFD relaxation when WUS is configured
  RRM relaxation for serving and neighbor cells
  DRX enhancements, e.g. dynamic DRX configuration, per serving cell DRX
  UE adaptation to PDSCH processing timeline, i.e. K1
  Additional UE assistant information
  Specific enhancements to FR2 and unlicensed spectrum operation
Further power saving enhancements for RRC_IDLE/INACTIVE state
  Paging enhancements, including paging WUS, reducing power consumption due to paging false alarm
  Further RRM power saving including serving cell RRM relaxation, additional RRM RS
  Longer DRX cycles
Note: whether and how to split the work between the Rel-17 UE power saving item and NR-light item should be further discussed

## Slide 4
Thanks