## Slide 1: Agenda Item : 9.4.21 Source : Samsung, CATT, Huawei, HiSilicon, NTT DOCOMO, ZTE Title : On the RAN4 LS to RAN on the MPE issue Document for : Discussion and Decision
3GPP TSG RAN meeting #85 RP-191954
Newport Beach, USA, September 16-20, 2019

## Slide 2: Background
The work on multi-beam in Rel.16 WID is as follows:
  Enhancements on multi-beam operation, primarily targeting FR2 operation:
    [MB1a] Perform study and, if needed, specify enhancement(s) on UL and/or DL transmit beam selection specified in Rel-15 to reduce latency and overhead
    [MB1b] Specify UL transmit beam selection for multi-panel operation that facilitates panel-specific beam selection
    [MB2a] Specify a beam failure recovery for SCell with DL/UL as well as DL-only, where PCell can be operating in FR1 as well as FR2 based on the beam failure recovery specified in Rel-15
    [MB2b] Specify measurement and reporting of either L1-RSRQ or L1-SINR
The following was agreed in RAN1#97 (Reno) as a response to RAN4 LS on MPE (first presented in RAN1 @RAN1#96bis) [1]:
  Down-select in RAN1#98 from the following options for beam management enhancements:
    Alt1. Support UE to report CRI/SSBRI where the CRI/SSBRI refers to a preferred spatial relation RS for UL transmission
      …
    Alt2. Support SRI field in the DCI can be used to indicate multiple SRS resources and UE’s autonomous selection of one SRS resource for PUSCH beam determination out of the multiple
    Alt3: Reuse Rel-15 beam specific PHR reporting to determine beam-specific MPE impact transparently, i.e., by difference value between Pc,max (which is calculated based on P-MPR) and the required transmission power.
      …
    Alt4: No enhancements considering MPE issues in Rel-16 RAN1 specifications. It is up to UE implementation in conjunction to RAN4 specicfiation support.
  If no consensus in RAN1#98, no further discussion in RAN1.

## Slide 3: Current status and general assessment
RAN1#98 conclusion (Friday Aug 30th) [2]:
  “On the issue of beam management enhancements to address MPE, there is no consensus in RAN1 to introduce additional specification support in RAN1. No further discussion for Rel-16 from RAN1 perspective” (emphasis added)
Assessment on MPE issue in RAN1:
  MPE issue has been presented over 7 RAN1 meetings and extensively discussed:
    A total of ~50 Tdocs, more than 7 hrs of focused offline/online sessions in the last 2 RAN1 meetings
    It was clarified that the issue is not whether a UE can meet MPE regulation, but whether the UL coverage loss (due to MPE regulation) can be effectively reduced by spec-based solutions
    Companies (e.g. Ericsson, Samsung, vivo [5]-[10]) have shown that even in the ideal and optimistic scenario, the UL coverage loss cannot be effectively reduced
  Divided position with “Alt4” representing the majority (~2x the support compared to Alt1/3) [3]

## Slide 4: Assessment on the RAN4 LS to RAN
RAN4 LS to RAN on MPE (agreed Friday Aug 30th) [4]:
  Drafted and agreed without a priori knowledge on RAN1#98 conclusion (made in parallel on the same day)
  “… to enable RAN4 solutions potentially impacting RAN1 and/or RAN2 specifications [Section 1]”, if intended for Rel.16 NR_eMIMO, may contradict the RAN1#98 conclusion
Re-adding MPE issue to Rel.16 NR_eMIMO WI is infeasible and detrimental to the completion of the WI:
  Potential RAN1/2 work could take place only after “RAN4 solutions” are available (no earlier than RAN4#92BIS 10/2019), leaving RAN1 with one WG meeting (RAN1#99 11/2019) before the completion of the WI
  New data on MPE issue is unlikely to take place  dramatic change in conclusion is unlikely
  A number of pending issues for NR_eMIMO require efficient use of the limited amount of remaining TUs

## Slide 5: Proposal for response to RAN4 LS
Proposal: RAN to send a response to RAN4 LS, stating that:
  In RAN1#98, RAN1 has reached the following conclusion on the MPE issue: “On the issue of beam management enhancements to address MPE, there is no consensus in RAN1 to introduce additional specification support in RAN1. No further discussion for Rel-16 from RAN1 perspective”
  RAN1/2 is not expected to perform any additional task related to MPE issue in Rel.16

## Slide 6: References
[1] 3GPP RAN1, RAN1#97 Chairman’s Notes
[2] 3GPP RAN1, RAN1#98 Chairman’s Notes
[3] 3GPP RAN1, R1-1909779, LG Electronics, Feature lead summary#4 of Enhancements on Multi-beam Operations
[4] 3GPP RAN4#92, R4-1910279, Nokia, Draft LS on enhanced FR2 MPE mitigation solutions for avoiding radio link failures and connection releases in Rel-16
[5] 3GPP RAN1, R1-1907436, Ericsson, Enhancements to multi-beam operation
[6] 3GPP RAN1, R1-1907476, Ericsson, Performance of P-MPR-aware multi-panel scheduling
[7] 3GPP RAN1, R1-1909225, Ericsson, Enhancements to multi-beam operation
[8] 3GPP RAN1, R1-1908502, Samsung, Enhancements on multi-beam operation
[9] 3GPP RAN1, R1-1908167, vivo, Further discussion on Multi-beam operation
[10] 3GPP RAN1, R1-1908169, vivo, Evaluation on P-MPR aware scheduling