## Slide 1: Discussion on the scope of IAB enhancements in Rel-17
3GPP TSG RAN Meeting #85
Newport Beach California, USA, September 16-20, 2019
RP-192000
Source: LG Electronics
Document for: Discussion
Agenda Item: 8.1.10

## Slide 2: 1. Introduction & motivation
Introduction
  According to the agreement in RAN#84 [RP-191551], discussion on IAB enhancement will start in September as a potential work area for Rel-17
  According to the agreement in RAN#84, work scope discussion for IAB enhancements include duplexing enhancement
  This paper introduces potential candidate areas for duplexing enhancements for Rel-17 IAB enhancement work scope discussion
Motivation of duplexing enhancements for IAB
  Rel-16 IAB allows only TDM between IAB backhaul link and access link
  Allowing simultaneous TX/RX between IAB backhaul link and access link may have benefits of
    Better scheduling flexibility at backhaul link and/or access link
    Reduced latency at backhaul link and/or access link
    Potential overall throughput enhancement for backhaul link and access link

## Slide 3: 2. Discussion
Candidates for duplexing enhancements for Rel-17 IAB
  Case 1) In-band SDM/FDM of backhaul DL and access UL
  Case 2) In-band SDM/FDM of backhaul UL and access DL
  Case 3) In-band simultaneous RX & TX on backhaul DL and access DL
  Case 4) In-band simultaneous TX & RX on backhaul UL and access UL

## Slide 4: 2. Discussion
Further enhancements to support enhanced duplex for IAB
  Backhaul-access resource allocation to support Case 1)~Case 4)
  Cross link interference (CLI) handling
    especially for case 1), handling interference btw backhaul DL RX and access UL RX at IAB node
    especially for case 3), handling interference btw backhaul DL RX and access DL TX at IAB node
    especially for case 4), handling interference btw backhaul UL TX and access UL RX at IAB node

## Slide 5: 3. Proposal
Proposal
  Consider the following cases as potential duplexing enhancements in the work scope discussion for Rel-17 IAB work area
    Case 1) In-band SDM/FDM of backhaul DL and access UL
    Case 2) In-band SDM/FDM of backhaul UL and access DL
    Case 3) In-band simultaneous RX & TX on backhaul DL and access DL
    Case 4) In-band simultaneous TX & RX on backhaul UL and access UL
  Consider the following enhancements to support duplexing enhancement for Rel-17 IAB work area
    Backhaul-access resource allocation to support Case 1)~Case 4)
    Cross link interference (CLI) handling