## Slide 1: Agenda Item: 8.2.5 Source: AT&T Title: Proposal for RAN Enhancements for New Deployment Models Document for: Discussion/Decision
3GPP TSG RAN Plenary Meeting #85 RP-192106
Newport Beach, USA: September 16-20, 2019

## Slide 2: Motivation
In Rel 16 various features such as multi-TRP, CA/DC enhancements have been developed however it is not easily possible to deploy these features since they either require a C-RAN like deployment or an ideal (0 latency) inter-connect between the DU.
In Rel 17 we would like to propose RAN enhancements for interface enhancements to allow for CU-CU and DU-DU coordination for uses cases to take advantage of Rel 16 feature.
UE
CC1
CC2
CA across gNB
UE
CC1 Lyr1
CC1 Lyr2
Multi-TRP across gNB

## Slide 3: Use Case 1: Inter gNB Multi-TRP
In Rel 16 RAN1 will specify various flavors of multi-TRP solution:
Multi-TRP with single DCI: Joint scheduling between 2 TRP e.g. same MAC between 2 TRP.
Multi-TRP with multi-DCI: Independent scheduling between 2 TRP with same or separate MAC. Solution for non ideal backhaul
Currently there is no low latency coordination mechanism between two MAC entities and in Rel 17 we propose to develop a mechanism for this MAC-MAC coordination in time-scales as required by the RAN1/RAN2 specification
DCI1
DCI2
PDSCH 1
PDSCH 2
CU
CU
DU
DU
DU
DU
UE
UE
Inter DU
M-TRP
Inter CU
M-TRP
X2
F1

## Slide 4: Use Case 2: Inter gNB CA
Aggregation between pico cell tier and macro cell tier is a very use case that allows operator to improve network performance in an effective way.
Currently the only way to do this is:
Ideal backhaul (e.g. C-RAN)
DC
Both the solution have limitations especially if the aggregation is between FR1 and FR2.
CU
CU
DU
DU
DU
DU
UE
UE
Inter DU
CA
Inter CU
CA
X2
F1

## Slide 5: Latency Tolerance of CA
CA is more sensitive to latency since the PCell and SCell scheduling are more closely tied. However with distributed scheduling it is still possible to get gain with non ideal backhaul.
CA is more sensitive to latency between the DU’s than DC (as expected)
10 + 10 MHz CA
2x2 MIMO
500m ISD
Typical X2 type latency might not be good enough for inter-site CA

## Slide 6: Summary
In Rel 17 architecture and inter-CU and inter-DU coordination techniques must be developed in order to take advantage of some of the RAN1/2 features developed in Rel 16.
Two of the key uses cases to focus on are:
Inter-DU and inter-CU multi DCI multi TRP solution
Inter DU and inter-CU CA
    FR1-FR2 CA
    FR1-FR1 CA