## Slide 1: Agenda Item: 8.1.14 Source: AT&T Title: Proposal for RAN Architecture and Enhancements for Slicing Document for: Discussion/Decision
3GPP TSG RAN Plenary Meeting #85 RP-192107
Newport Beach, USA: September 16-20, 2019

## Slide 2: RAN Architecture Enhancements for Slicing
While Rel. 15 provided specifications for RAN support of network slicing, further enhancements should be made in Rel. 17 to the RAN architecture to simultaneously support different types of traffic (e.g. eMBB, URLLC) with different latency, reliability, and data rate requirements
Network Slicing at the RAN
Configuration of RAN resources to support different slices
Support different RAN architectures on the same HW via RAN enhancements to slicing
RP-192107

## Slide 3: Architecture to Support Different Protocol Splits for Different Slices
uRLLC
RF
MAC
PHY
RLC
RAN Remote Unit
Network Slice 2
Network Slice 1
eMBB
RF
MAC
RLC
Core
PDCP
Core
Virtual Infrastructure
RAN Distributed Unit
Virtual Infrastructure
RAN Central Unit
PDCP
SDAP
SDAP
PHY-Hi
PHY-Lo
UE
Latency requirements for URLLC and eMBB, for example, can imply that the deployed RAN architecture to support the two network slices can be different. It is not, however, desirable to have different network architectures for URLLC and eMBB.
Proposal: Architecture enhancements to simultaneously deploy different functional splits for different slices supporting different types of traffic on the same hardware
RP-192107

## Slide 4: Examples of Different Architectures with Different Functional Splits
2 gNB-DUs with 2 separate MACs
Exchange of information between gNB-DUs
Hierarchical gNB-CU/gNB-DU scheduling
Split cell architecture.
One gNB-DU with a lower MAC at the edge
Hierarchical gNB-CU/gNB-DU scheduling
Separate MACs Architecture
gNB-CU
gNB-DU
gNB-DU
MAC
RLC
PHY-Hi
RF
MAC
PHY
RLC
gNB-CU
gNB-DU
RLC
MAC-hi
MAC-lo
RF
PHY
gNB-RU
PHY-Lo
Split Cell Architecture
RP-192107