## Slide 1: Rel-16 UE Power Saving
China Academy of Telecommunications Technology (CATT)
3GPP TSG RAN Meeting #85 RP-192250
Newport Beach, USA, September 16-20, 2019

## Slide 2: Summary of Offline Discussion
1 TU for RAN2#109 is added
TS38.304 and TS38.306 are added to the list of impact existing TR/RS
No consensus on the removal of UE assistance information of SCell and BWP from the WID
Handling of UE dormancy behavior in NR DC/CA
  RAN2 agreements on dormancy behavior in support of power saving purpose for fast SCell activation
    SCell dormant state like LTE euCA will not be introduced in NR.
    ‘dormancy’ behaviour will be studied as a solution for fast return to SCell utilisation for data transfer. The 'dormancy' behaviour implies that the UE stops monitoring PDCCH but continues other activities such as CSI measurements, AGC and beam management. RAN1/4 input required on feasibility and benefit.
  RAN1 agreements
    From RAN1 perspective, L1 based mechanism for transitioning between ‘dormancy-like’ and ‘non dormancy-like’ behavior on activated Scells can be supported
    ‘dormancy-like’ => sparse/no PDCCH monitoring on activated Scell while maintaining CSI measurements/reporting
There are different views on which WI to contain the power saving of reducing PDCCH monitoring for activated SCell in the fast SCell activation

## Slide 3
Reference

## Slide 4: Power Saving Signal/Channel
UE monitoring on Power Saving Signal/Channel before DRX per MAC entity
  UE is indicated to wake up to a MAC entity, which includes all cells in CA
  RAN2 agreements on the study of UE dormancy behavior of activated SCells for UE power saving purpose
    RAN1/RAN4 agree on the feasibility of UE dormancy behavior
    RAN1 agreement
      From RAN1 perspective, L1 based mechanism for transitioning between ‘dormancy-like’ and ‘non dormancy-like’ behavior on activated Scells can be supported
      ‘dormancy-like’ => sparse/no PDCCH monitoring on activated Scell while maintaining CSI measurements/reporting
    the L1-based signaling is used as the indication of UE dormancy behaviror
DRX ON
DRX ON
DRX ON
PCell
SCell 1
SCell 2
Indication by
Power saving signal/channel
Outside Active Time
Reducing PDCCH monitoring
DCI as the indication of
Power saving techniques, WUS, etc

## Slide 5: Indication of SCell Dormancy inside Active Time
Power saving signal/channel as the indication of PDCCH monitoring of selected SCell
  Power saving signal/channel is the enhancement of existing DCI
  RAN1#98 agrees to have 1-bit indication for the dynamic switching of same slot and cross-slot scheduling.
DRX ON
DRX ON
DRX ON
PCell
SCell 1
SCell 2
Power saving signal/channel based on enhancement of Scheduling DCI
Dynamic switching between Cross-slot and same slot scheduling
SCell Dormancy
Indication of
Power saving techniques,
Scheduling
DCI

## Slide 6: UE Assistance Information on SCell/BWP
During UE power saving study, power saving gain is shown with UE assistance information on SCell grouping
  Power saving gain was shown on a group of SCells through the shared components in RF processing chain
    Different UE implementation in RF processing chains on the different carriers in CA/DC
    UE assistance information is to feedback the cells in a cell group to achieve power saving from the shared components.
  UE assistance information on SCell grouping