## Slide 1: Title: FR2 specific higher layer enhancements for REL-17
Sep 2019, RAN #85
Source: Samsung, KDDI, KT, Intel, SK telecom, LG Uplus, Verizon
RP-192256

## Slide 2: Introduction/Discussion
NR standardization has been successful and is continuously evolving to meet the most prominent industry demand. Rel-15 NR provides the basic frameworks focusing on MBB and URLLC. Rel-16 NR is being extending further to various verticals.
FR2/High Frequency is the landmark feature for NR. It has been considered impacting mainly physical layer. However, FR2 performance can be significantly enhanced by improving higher layer specific aspects.
In the Annex, we present potential areas for the enhancements.
  Enhancements on RLM/BFD on FR2 serving cell
  Enhancements on random access in FR2 cells
  Enhancements on configured grant in FR2 serving cells
  Enhancements on FR2 SCell activation
  Enhancements on HO interruption time reduction for FR2
It is not the exhaustive list. Further discussion to have consolidated views on the scope is desirable.
The works cope should be elaborated to avoid duplicate work in any other Rel-17 items.

## Slide 3: Suggestions
To achieve what FR2 is supposed to achieve, higher layer aspects shall be put on the places as well.
We believe REL-17 is the release, if not too late, to do this.
Proposal 1: To agree that higher layer specific FR2 enhancements will be studied and specified in REL-17
Proposal 2: To have an e-mail discussion until Dec to form consolidated views on the work scope

## Slide 4: ANNEX. POTENTIAL AREAS FOR ENHANCEMENTS

## Slide 5: Enhancements on RLM/BFD on FR2 serving cell
Problem to be addressed
  Radio Link Monitoring and Beam Failure Detection are defined as a function DRX cycle length.
  Due to fast changing channel condition in FR2, longer DRX cycle (>160 ms) would degrade the RLM/BFD performance significantly (i.e. several seconds taken until recovery action is executed during while the connection is completely lost)
Possible way to address the problem (not exhaustive)
  Adjusting the length of phase 1 and phase 2 to trigger recovery quickly when necessary
 | Radio Link Monitoring | Beam failure detection
Phase 1: Detecting the problem RLM: > 20 * DRX cycle BFD: > 10 * DRX cycle | TEvaluate_out_CSI-RS = ceil(Mout×P) × TDRX Mout = 20 L1 evaluation whether all of RLM-RS resource is worse than Qout_CSI-RS during TEvaluate_out_CSI-RS | TEvaluate_BFD_CSI-RS = [MBFD *P*N] * TDRX, MBFD = 10 L1 evaluation whether all resource in set q0 is worse than Qout_LR_CIS-RS during TEvaluate_BFD_CSI-RS
Phase 2: Conforming the problem RLM, BFD: ≈ 10* DRX cycle | N310 * TDRX; N310 =[n1 ~ n20] L1 indicates N310 times out of sync indication to L3; | n * TDRX, n =[n1 ~ n10] L1 indicates beamFailureInstanceMaxCount times beamfailureindication to L2;
Phase 3: Preparing the recovery | T310 = [ms0 ~ ms6000] L3 starts T310. When T310 expires, RLF is triggered. When 310 runs, L1 still measure RLM-RS resource | TEvaluate_BFD_CSI-RS = ceil(MCBD *P*N) *TDRX, MCBD = 3 L1 evaluates whether set q1 is usable during TEvaluate_CBD_CSI-RS
Phase 4: Executing the recovery | RRC connection reestablishment is triggered | Random Access (either contention free or contention based) for beam recovery is triggered

## Slide 6: Enhancements on random access in FR2 cells
Problem to be addressed
  Random access is designed with single preamble single RAR principle
  In a system without beam correspondence, UE needs to perform preamble transmission/RAR monitoring multiple times until beam is synchronized
Possible way to address the problem (not exhaustive)
  Multiple preambles are transmitted together within a short time duration.
RAR monitoring
RAR reception
RAR monitoring
RAR reception
detected by GNB
detected by GNB
RAR monitoring

## Slide 7: Enhancements on configured grant in FR2 serving cells
Problem to be addressed
  Configured grant is configured per BWP. For type 1CG, RRC procedure is used to allocate/update/release the resource.
  The beam direction could change in a BWP. If a UE is configured with CG, and the RX beam of gNB needs to be changed, the resource may not be utilized for the new beam. Then, gNB has to explicitly update the resource by RRC, which may result performance degradation.
Possible way to address the problem (not exhaustive)
  Define configured grant per BWP per beam(s)
UE A moves
gNB
UE A
UE B
gNB
UE A
UE B
R1
R2
time
UE B
UE A
gNB receives from UEs A & B using B1
Rx Beam: B1
Rx Beam: B1
Rx Beam: B2
R2
time
UE B
gNB may not be able to use R1 for B2, and need a different time slot to use B2 for UE A.
R1
UE A

## Slide 8: Enhancements on FR2 SCell activation
Problem to be addressed
  FR2 SCell activation may take much longer time than FR1 SCell activation due to potential Rx beam sweeping in UE
Possible way to address the problem (not exhaustive)
  Rel-16 DC/CA enhancement is discussing dormancy behavior where UE keep measuring periodic CSI-RS and reporting CSI. It can reduced the FR2 SCell activation significantly at the cost of UE power.
  More efficient way is to utilize the burst aperiodic CSI-RS corresponding to multiple beam sweepings.
If Rel-16 turns out to address the issue properly, it can be taken out of the list.

## Slide 9: Enhancements on HO interruption time reduction for FR2
Problem to be addressed
  Simultaneous connectivity will be introduce to reduce HO interruption time in Rel-16 mobility enhancement WI.
  However, simultaneous connectivity option will not be applied for FR2
    In Rel-16, the WID NR mobility enhancement aims to reduce HO/ SCG change interruption time and to improve HO reliability. However RAN4 concluded that handover with simultaneous transmission/reception is not feasible in FR2, and RAN2 will not work on it in Rel-16.
  Reducing HO interruption time is important in FR2 as well especially considering small size cell in high frequency.
Possible way to address the problem (not exhaustive)
  Simultaneous connectivity without requiring simultaneous transmission/reception.
    One possible way is TDM i.e. the UE receives/transmits from/to source and target cell in different timing during the HO.