## Slide 1: 5G AV Production Possibilities
European Broadcasting Union

## Slide 2: What are we looking at?
Notes: We already use a lot of wireless tools in production, radio mics capture high quality sound for amplification or recording, Radio Cameras are used at large events to enhance the production experience. We also use satellite links to transmit content from the field back to a broadcast centre for distribution and radio talkback is used to communicate between team members on the ground. Finally 3G and 4G bonded cellular contributions are now commonplace in news workflows where multiple sim cards are used to get the bandwidth required to transmit a highly compressed video stream.
we have workflows for this already so any 3GPP system needs to be as good as or improve on existing workflows while maintaining costs of deployments. We are exploring this technology because we recognize that spectrum is at a premium and some 5G deployments may reduce costs or add flexibility or mobility

## Slide 3: Summary
High Bandwidth uplink requirements
  Uncompressed UHD video 12.5 Gbit/s used in point to point FWA links
  Compressed UHD Video 200 Mbit/s used on mobile radio camera
  Compressed HD Video 50 Mbit/s used for high quality contribution
Low-latency
Real-time control tactile requires < 10 ms
Frame synchronisation across multiple cameras requires < 6 ms
Audio has tighter requirements (< 600 us RTL for a radio mic/IEM combo)
Predictable constant latency is essential
Reliability
The effect of packet losses is propagated through the entire production chain (PER of 10^-14)
Any Packet loss results in unacceptable audio glitch's or freeze frames
Notes: High bandwith uplinks. Video and audio signals can be require large amounts of data and for production it is mostly uplinked so uplink traffic may well exceed downlink traffic by a factor of 20 to 1
Low latency, a number of AV prod user cases have very low latency requirements in addition they need to be synchronized so that the latency is predictable, a variable latency between 2 or more devices will mean that they drift in and out of synch and therefore become unusable in a production scenario
The loss of packets leads to picture break up or freezing of a picture or severe clicking or noise on an audio source. In order to maintain the use of a source the loss of packets must be near zero measured at the received point. This is often more critical than latency so a small amount of retransmission is allowed
Reliable links are also expected so SNPN deployments are expected to be common place
Having a predictable latency is more important than minimizing individual streams for example a 5mS latency across all devices is easier to cope with than several devices that may be 100,200 or 300 uS
final note:

## Slide 4: Summary
Multicast
Use cases and low latency (< 3 ms) is required (eg intercom systems)
Easy deployment of SNPN
Onboarding
Alternative identities
Reliable wireless backhaul
Moving base stations, e.g. in an airplane or on the ground
Synchronization
Video and audio sources often needs tight synchronization for editing, mixing, video and audio sources
Source of PTP (accuracy< 1us ) for UE to act as a master-clock to enable synchronisation
Notes: Current ways of working with radio equipment mean that the functions provided by a multicast or broadcast system are expected, a director wants to be able to talk to multiple people at the same time and any response heard by the whole talkgroup. Latency is critical as when a camera move is asked for or a lighting cue requested it has to happen at a single point in time.
Because of the type of activities we expect to deploy our own standalone Non-Public Networks this means we need to have provisiosn for UE’s to securly join the networks and understand their functionality, they may be required to join several networks simultaneously such as a radio mic at a concert which may connect to a broadcast mix, a PA mix and a monitor mix
It is also important that video and audio is syncronised to avoid lip sync errors, where multiple cameras are deployed they must be timed together to avoid issues where shutters are not opening and closeing together or where frames jump as one camera cuts to another

## Slide 5: Work to Date
Study item: Audio Video Production (FS_AVProd)
TR 22.827
100% complete, presented to SA#85 for approval
13 video and audio user cases
Focus on new requirements not existing specs
Work Item: Service requirements for Video, Imaging and Audio for Professional Applications (VIAPA)
TS 22.263
Performance metrics for audio and video
Combines CMED (Communication Services for Critical Medical Applications) user cases that also have high performance requirements (TR 22.826)
Change requests to existing specs (TS 22.261)
80% complete, presented to SA#85 for information
Notes: Work to date
Now completed TR but while this covers user cases that push the requirements it does not cover every area where content producers may use 5G for example high speed high bandwidth file transfer which does not have a real time metric
The next item is SA1 WID that includes the viapa service specs as well as matching requirements to existing functionality where possible and creating change requests where appropriate.
For the VIAPA service requirements we have looked see where other verticals have similar requirments and incorporated those so as to avoide separate TS for every vertical. The first iteration of this is for medical applications but others may follow.

## Slide 6: RAN impact
High bandwidth uplinks
  Video and audio contribution
IIoT and URLLC enhancements
  Low latency, high density and efficiency
Integrated Access and Backhaul enhancements
  Managing connectivity in a mobile SNPN either air or ground based
NR multicast broadcast
  Low latency communications systems
Network slicing
  Dedicated media contribution networks
  SNPN in studios and on location
Coverage enhancements
Sidelink enhancements.
  Device to device communications for radio mics or video monitoring
Notes: We have looked at items currently in Ran and see these as the important ones for Avprod.

## Slide 7
Bonded Cellular
Used by News
Heavily Compressed
High Latency (up to 5 seconds)
Single camera contribution
Constrained flexibility
Notes: Already widely used but has constraints picture quality is constrained by available bandwidth and the use of multiple data connections means that specialist kit is required at both ends of the chain this is linked by manufacturer specific UE and so reduces flexibility on what equipment is available at both transmit and receive sites. It is also a single source link so it is not possible to combine multiple cameras on site easily and so specialist kit is sent on location to combine multiple camera feeds into a single feed.

## Slide 8
Radio Mics and IEM
Very Low Latency (<
synchronized
Multiple deployment
Notes: Radio mics are very challenging with requirements for extremely low end to end latency >5ms. It is important that a a performer wearing in ear monitors does not hear an echo on their voice as this makes speaking impossible. They are also often deployed in close locations with other radio mics, a large show may have up to 50 radio mics and/or wireless instrument links at use at one time and often the audio may need to go to multiple receive points (such as a PA mix and a broadcast mix) audio is often synchronized with other audio sources and video so a requirement for thm to stay in synch is also essential. In most instances a SNPN is envisioned.

## Slide 9
Radio Cameras
Very Low Latency
synchronized
Very high reliability requirements (PER 10^-14)
High Bandwidth up link (up to 200 Mb/s)
Notes: Radio Camera are used where it is not always possible to wire a camera. Eg a Steadicam on the touch line of a large sporting event or on a motorbike for a cycle race or marathon. They have to be extremely low latency to match cameras that are connected via fibre and also so that a director can expect an instant response when they request a camera move. There is also a requirement for some operations such as colour settings to be controlled remotely so a 2 way communication is used. Uplink bandwidth is key to maintain image quality as set out in TR 22.827. on large scale deployments these may be on Motorbikes and the signal transmitted to a relay aircraft. It would be useful to deploy this type of scenario using an SNPN in order to avoid contention on a PLMN but there may be scenarios where a single camera unit may be required to switch between 2 networks in a seamless manor where the networks support the functionality. Where multiple cameras are deployed it is vitakl that they remain in sync with each other and so a PTO time signal is used to

## Slide 10
Talkback
Very Low Latency
‘Broadcast mode’
PTT and listen only
Notes: For all staff to communicate on a production a high reliability low latency comms system is deployed known as talkback. It is nessacary for a director to be able to talk to different talk groups as well as communicate with a production team as a whole. Broadcast mode within a single cell area

## Slide 11
Contribution
Low Latency
High reliability
High uplink bandwidth
  Up to 12.5Gbit/s uncompressed
  Up to 200 Mbit/s compressed
Notes: Current links from events are often sent back via fibre or satellite vehicles. While the video signal is compressed the general rule is to use the minimum compression possible as this will degrade the picture and in some cases make it unsuitable for transmission on a distribution network using lower bit rate codecs