## Slide 1: On pi/2 BPSK waveform generation RP-192403 IITH, Reliance Jio, IITM, CEWIT, Tejas Networks

## Slide 2: Background
Rel-15 and Rel-16 support pi/2 BPSK transmission in UL
PUSCH supports multiple-port transmission in Rel-15 and Rel-16
Rel-15 uses ZC sequence as DMRS
Rel-16 uses low PAPR pi/2 BPSK based sequences for DMRS
Spectrum shaping/filtering is optional and is described in RAN4 specifications. No mention in RAN1 specifications
Problem:
  There is UE TX spec ambiguity for PUSCH transmissions for both Rel-15 and Rel-16
  Unless resolved, pi/2 BPSK PUSCH feature remains broken in 3GPP Rel-15 and 16 specifications

## Slide 3: Typical pi/2 BPSK PUSCH Chain with Filtering
Binary Data
BPSK Modulation
Filter
DFT
Subcarrier Mapping
IFFT
CP Addition
This filter is transparent in the spec;
only spectrum flatness is defined in RAN4

## Slide 4: Principles
Let f be the filter e.g. [0.28 1 0.28] or [1 1]
  The exact filter coefficients are out of spec scope.
Consider 1 PRB transmission of PUSCH i.e., 12 tones
  DMRS length = 6 tones
Spec supports 2-port transmission on port-0 and port-1 for PUSCH
Identical Filter must be used on data and DMRS for correct data detection for all ports

## Slide 5: Illustration of the Problem for length=12 allocation
Let F be the frequency domain representation of f
  For 1 PRB transmission, length of F is 12
  F = [F0, F1, F2, F3, ………, F11 ]
  Define Feven = [F0, F2, F4, F6, F8, F10] and Fodd = [F1, F3, F5, F7, F9, F11]
Data uses F on 12 allocated tones
DMRS with length=6 on Port-0 transmission may use Feven
Question: Should DMRS Port-1 transmission use Feven or Fodd ???
  What if different UE vendors use different filters for port-0 and port-1?
  What should gNB receiver do?
Spec needs to bring clarity for correct demodulation