## Slide 1: Spectrum sharing between NR and LTE re-farming band
Samsung, Apple, Comcast, CableLabs, Federated Wireless, Charter Communications

## Slide 2: Agreement on generic principle for DSS
DSS in LTE re-farming bands, including existing NR bands and new re-farming bands in the future, should be in line with NR global channel raster and sync raster design;
DSS in existing LTE re-farming bands should not change existing band specific channel raster and default sync raster entries;
Changes, if any, in existing LTE re-farming bands should be analyzed for backward compatible issues;
If needed, new bands can be considered following same principle as for e.g. band n41/n90.

## Slide 3: Agreement on DSS in existing LTE re-farming bands
Band specific channel raster and sync raster:
  As a main principle, no changes to existing definitions;
  If changes are needed, then a new band approach can be adopted similar to band n41/n90.
UL 7.5 kHz shift:
  need to be checked in a case by case manner;
  if no NBC issue identified i.e. no early UE support this NR bands, UL 7.5kHz shift can be applied to this band;
  If NBC issue identified, new band approach can be adopted similar as band n41/n90.

## Slide 4: Agreement on new LTE re-farming bands in the future
Channel raster:
  For bands below 3GHz, NREF in 100kHz step can be used;
  For bands above 3GHz, NREF in 300 kHz step can be used;
Whether need to support default SSB with 30kHz SCS and SSB block pattern B can be discussed in a case by case manner;
7.5 kHz UL shift should be mandatory supported for newly introduced LTE re-farming bands for DSS purpose only.

## Slide 5: Proposals on DSS for band 48/n48
Channel raster
  No change to channel raster because 300kHz granularity can be already configured by the network;
Sync raster:
  Option 1: MBSFN approach can be used to avoid transmission collisions between NR SSB and LTE CRS (no specification changes);
  Option 2: introduce sync raster B (requiring specification changes);
UL 7.5 kHz shift:
  Since there are no backwards compatibility issues with this band, make UL 7.5 kHz shift mandatory for n48
With above changes DSS for band 48/n48 can be supported without new band introduced.
NOTE: at least in RAN4#92bis, there is no vendor declare on deployment of device in band n48