## Slide 1: Title: MakeBeforeBreak support in NR
Sep 2019, RAN #86
Source: Samsung, KDDI, Verizon
RP-192438

## Slide 2: Introduction
MakeBeforBreak is a simple protocol centric enhancement to reduce the handover interruption time.
LTE supports MBB since Release 14.
NR enhance mobility with Release 16 WI mobility enhancement.
NR mobility enhancement does not support MBB with the understanding that
  Dual Active Protocol Stack achieves better performance.
  DAPS is frequency agnostic (i.e. applicable to both FR1 and FR2)
DAPS requires simultaneous Tx/Rx both with the source node and the target node. It later turned out not applicable to FR2.
Since DAPS is only solution to be defined for NR mobility enhancement in terms of handover interruption reduction, FR2 is left without any enhancement for this aspect.

## Slide 3: Make Before Break
In the conventional handover, UE tear down the source link immediately upon receiving Handover Command. PRACH periodicity is up to 160 m sec in FR2. Hence UE may need to wait 160 m sec before transmitting the preamble in the target node.
In MBB, UE maintains the source link until it transmits the first preamble in the target. Hence 160 m sec interruption is removed.
UE
Source
Target
Handover Command
PRACH preamble
Break the source link
DL synch
Wait until the first PRACH occasion (could be 160 msec in FR2)
<Handover>
UE
Source
Target
Handover Command
PRACH preamble
Break the source link
DL synch
Wait until the first PRACH occasion (could be 160 msec in FR2)
<Make Before Break>
Not break the source link
Interruption
No interruption

## Slide 4: Suggestion
MBB is protocol centric enhancement. Spec impact is minimal. No H/W impact.
NR RRC CR for MBB [1], which is just mirror of LTE MBB CR, has been around for many RAN2 meetings.
RAN2 has one meeting remaining to complete NR mobility enhancement.
It may be challenging but not impossible to introduce MBB in Release 16.
If MBB is not specified, FR2 is left with no enhancement on interruption reduction even though interruption is more sever in FR2.
Proposal: RAN task RAN2 to specify LTE MBB like enhancement under NR mobility enhancement WI.

## Slide 5: Reference
[1] R2-1916087 Introducing Make-Before-Break in NR Samsung