## Slide 1: Efficient Delivery of Public Service Media Content & Services over 3GPP Networks
EBU, BBC, IRT

## Slide 2: Background
Broadcasters deliver linear/live audio/visual content over terrestrial broadcast networks today
  e.g. using DVB-T, DVB-T2 or DAB+
Broadcasters also deliver linear/live and on-demand audio/visual services over the internet (i.e. OTT)
  Including mobile networks with applications such as BBC iPlayer, BBC Sounds and ARD/ZDF Mediathek

## Slide 3: Examples of OTT portals from broadcasters
Live Video programmes
On-demand Video programmes

## Slide 4
Live Video programmes
On-demand Video programmes

## Slide 5
Live Audio programmes
On-demand Audio programmes

## Slide 6: Requirements
Inclusion of multicast/broadcast capabilities in NR-RAN may ensure an efficient connection 5G Core to deliver PSM content with high QoS, particularly at times of peak audience demand, and with a decreased overall network load

## Slide 7: Considerations regarding Rel-17 RAN features
Solutions in 3GPP NR should facilitate forward compatibility such as e.g. 100% broadcast/multicast carrier operation and free-to-air.
Specify multicast/broadcast in 3GPP NR to deliver point-to-multipoint audio/video services with appropriate QoS and at scale.
  Spectrally efficient multiplexing of multicast and unicast;
  Realise point-to-multipoint delivery enabling multiple UEs to receive common traffic;
  Concurrent reception of unicast and multicast;
  Reusing Unicast transport channels, control channels and signals where possible;
Study solutions to maximize spectral efficiency and coverage areas for mixed multicast/broadcast carriers and/or a combination of mixed multicast/broadcast carriers and unicast carriers in different parts of the network, in particular to guarantee service continuity across large areas and sustained QoS between adjacent cells. In particular, considering interference management solutions such as:
  Single Frequency Network (SFN) over small number of cells; and/or
  Coordinated MultiPoint transmissions (CoMP); and/or
  Any other techniques that might prove beneficial in the scope of this study
Note: All these requirements have been specified in 3GPP TS 22.101, clause 32 and TR 38.913, clause 9.1

## Slide 8: Conclusions
Include broadcast/multicast as a feature in Rel-17 NR
Include delivery of audio/video services in the scope of any Work or Study Items relating to this feature
We support an 18-month time period for Release 17