## Slide 1
Views on NR light in Rel-17
3GPP TSG-RAN WG Meeting #86
Sitges, Spain, Dec 9th-12th, 2019
RP-192539

## Slide 2
NR Light – Use cases and design targets requirements
  Use cases
    Smart wearables, e.g. smart watch, glasses, health care
    Smart home appliances
    High end MTC
    Low end smartphones (if “low-tier UE” is not introduced in REl-16)
  Key design requirements
    Peak data rate: target peak data is scenario dependent.
      For smart wearables [10~100Mbps],
      For low end smartphones >200Mbps
    UE power consumption, 1~2 week battery life for smart watch with typical usage (not standby only), with low battery capacity (e.g. <500mAh)
    Reduced device complexity, cost and size
    Typical eMBB service latency
    Seamless switching/service continuation across different devices, especially for wearable use case, e.g. a voice call to a smart watch can be switched to a smartphone without significant interruption, or vice versa.
  The potential use cases for NR-light UEs are expected to be diverse, it is important to have a study phase(e.g. a study item) to discuss and document the different use cases together with the key design requirements/targets.

## Slide 3
NR Light – Proposed objectives
  Study and specify the following UE complexity reduction techniques,
    Reduced UE supported BW by reusing Rel-15 initial access design, e.g. DL BW down to 5MHz/10MHz for 15KHz/30KHz in FR1. Decoupling of UE supported DL and UL BW.
    Efficient operation for reduced bandwidth UEs in a wideband system, including co-existence with wideband UEs.
    Reduced UE Rx antennas, including 1Rx and 2Rx
    New UE power class with lower Tx power
      Integrated transceiver and PA design can be enabled by a lower Tx power class (~15dBm), which provides significant benefit for reducing device size and cost
    PDCCH monitoring capability reduction
    Relaxed UE processing time capability
    Potential UE categories targeting different data rates
  Study and specify the following
    Coverage compensation focusing on coverage loss due to NR-light features, for example reduced UE Rx antenna, reduced BW, lower UE Tx power class
      Work split with coverage enhancement SI/WI?
    Seamless switching/service continuation across different devices
      e.g. voice call switching between smartphone and watch, paging loss,…
  Further UE power saving, e.g. IDLE mode paging enhancements, RRM relaxation, etc
    Work split with UE power saving WI?

## Slide 4
THANK
YOU