## Slide 1
Views on NR UE power saving in Rel-17
3GPP TSG-RAN WG Meeting #86
Sitges, Spain, Dec 9th-12th, 2019
RP-192540

## Slide 2
Further UE power saving – Background
  Basic UE power saving features provided in Rel-15
    Bandwidth part adaptation
    DRX
    RRC_INACTIVE state
    Configurable PDCCH monitoring periodicity
  Enhanced UE power saving features provided in Rel-16
    UE adaptation in RRC_CONNECTED state
      Basic WUS function: Wake-up PDCCH to trigger UE activity for the next DRX ON cycle
      L1 based UE adaptation between same-slot and cross-slot scheduling
      L1 based UE adaptation to the maximum MIMO layer
      L1 based UE scell adaptation between “dormancy” and “non-dormancy” behaviours using WUS (outside active time) or DCI (active time) (MR DC/CA)
      UE assistant information for state transition and some DRX parameters
      Dual cDRX operation in CA (discussed in Rel-16 TEI)
    RRM relaxation for neighbour cells in RRC_IDLE/INACTIVE state
  Further UE power saving should be considered in Rel-17 for different RRC states
    Enhancements to RRC_CONNECTED state is beneficial for all UE types (smartphone, wearables)
    Enhancements to RRC_IDLE/INACTIVE state is especially beneficial for NR light devices (e.g. wearables, MTC)

## Slide 3
Further UE power saving –Proposed objectives
  Further power saving enhancements for RRC_CONNECTED state
    Enhanced WUS function to indicate UE adaptation e.g. maximum MIMO layer, BWP
    PDCCH monitoring reduction during DRX active time
    RLM/BFD relaxation when WUS is configured
      RLM/BFD consumes significant amount of UE power, see evaluations in R1-1912799 (also attached for convenience)
      Potential solutions
        RLM/BFD relaxation, i.e. not mandated every DRX cycle, or
        RLM/BFD measurement performed during WUS monitoring
    RRM relaxation for serving and neighbor cells
    UE adaptation to PDSCH processing timeline, i.e. K1 adaptation for UE capable of CAP#2 timeline
    Enhancements to FR2 (e.g. more efficient WUS beam sweeping)
    Additional UE assistant information
  Further power saving enhancements for RRC_IDLE/INACTIVE state
    Paging enhancements, including paging WUS, reducing power consumption due to paging false alarm
    Further RRM power saving including
      serving cell RRM relaxation, as a continuation from Rel-16
      additional RRM RS (without NW OH increase, e.g. network to broadcast the presence of CSI-RS to IDLE mode UEs)

## Slide 4
THANK
YOU