## Slide 1
Views on NR MIMO in Rel-17
3GPP TSG-RAN WG Meeting #86
Sitges, Spain, Dec 9th-12th, 2019
RP-192541

## Slide 2
Multi-beam enhancement
Study beam failure recovery enhancement for intra- and inter-cell mobility, including beam failure detection latency reduction
To reduce overhead and latency of DL and UL beam management, unified TCI framework for DL/UL beam indication, e.g. SRS resource is used as QCL source of DL signal, UL beam indication by CRI/SSBRI instead of SRI in DCI for PUSCH.
Study event triggered DL and UL beam management procedures
  Define new event for UE initiated BM or for partial BFR, TRP specific BFR, PCell+SCell BFD.
Multi-panel @UE
  From UE implementation perspective, deploying STxMP is very challenging!
  Simultaneous reception across multi-panel can be supported
  Panel selection/activation/switching for Network and UE’s alignment and power saving, including UE initiated panel switching on/off.
  Support panel specific power control. Decouple UL timing from multi-panel issues and study timing for multi-TRP or for mobility cases.
Some specification support to address MPE issues in Rel-16, further enhancement in RAN1 is not clear at this moment.

## Slide 3
Multi-TRP enhancement
Enhancement on the support for multi-TRP deployment, targeting both FR1 and FR2:
  Support of improving reliability and robustness for PDCCH, PUSCH, and PUCCH including channel repetition and/or simultaneous transmission
  FR2-specific enhancement for multi-TRP
    Beam reporting and beam indication in multi-TRP considering the UE supporting different MPUE capabilities, and progress in multi-beam enhancement
    BFR enhancement for multi-TRP
  Enhancement of inter-cell multi-TRP operations
    Inter-cell multi-TRP should be considered together in the scope of L1/L2-centric inter-cell mobility
  Further enhancement of PDSCH to improvement spectrum efficiency and robustness
    Enable multi-DCI based PDSCH repetition
    Support of joint schemes between scheme 4 and other URLLC schemes
    Enhancement of robust rank>=2 MIMO transmission in high speed scenario
    Enhancement of SFN based transmission in high speed scenario

## Slide 4
UL MIMO enhancement
Enhancement on SRS transmission and flexible triggering
  Aperiodic SRS triggering offset is RRC configured in NR, which is less flexible than LTE
  NR supports SRS configuration for different purposes, e.g. beamManagement, codebook, nonCodebook, antennaSwitching, SRS for one purpose can be utilized for other purpose in order to save overhead
  Rel-16 NRU already supports SRS configuration on all 14 symbols of the slot for capacity enhancement
  No strong motivation on enhancing precoded SRS, UE RF chains are non-coherent in real deployment
Enhancement on UL precoding, PAPR reduction, power imbalance
  Support of UL frequency selective precoding
  Mechanism for PAPR reduction in UL PUSCH transmission
  Address power imbalance issue in UL where there could be significant power variance between 2 symbols (see appendix)
Enhancement of UL system performance
  UL receiver performance may degrade significantly when interference is not taken into account (some analysis and evaluation results can be found in appendix)

## Slide 5
Appendix - UL frequency selective precoding
Sub-band
Precodeding/
phase rotation
Sub-band
Precodeding/
phase rotation
Sub-band
Precodeding/
phase rotation
Scheduled UL resources

## Slide 6
Appendix – Power imbalance

## Slide 7
Appendix – MMSE IRC receiver
The uplink receiver signal for UE index m
MMSE-IRC equalizer for UE m
is estimated based on DMRS with some PRB size (e.g size=1)

## Slide 8
Interference on DMRS and PUSCH
In general, it is always assumed that DMRS and PUSCH suffer from the same interference, which is tenable for uplink in LTE. However, this assumption may not valid anymore in NR, since the DMRS configuration including the position in time domain and pattern in frequency domain is flexible, also depends on the type of PUSCH. So, the performance of MMSE-IRC can degrade if it is not taken care of.
For example, UE1 is target user in serving cell1, and on the same slot UE2 in cell2 will generate interference to UE1; half of PUSCH OFDM symbols were polluted by colored noise (interference), where are other half of the PUSCH symbols and one DMRS symbol are polluted by white noise.
DMRS

## Slide 9
Simulation assumptions
Wireless channel | TDL-A
BS configuration | 8 antennas with dual polarization and low correlation
UE antenna configuration | 2 Tx
RI and PMI and AMC | Adaptive with BLER=10%
PUSCH | UE1 with typeA, 7symbols UE2 with typeB, 7symbols or 3symbols
SIR | Means the ratio of the transmitter power of UE1 to UE2(as interference)
SRS period | 40 slots
channel estimation | 2D-MMSE filter
equalizer | Traditional MMSE-IRC detection, without any apriority information for interference

## Slide 10
Evaluation results
Case1： UE1 with typeA (7symbols) and UE2 with typeB (7symbols), full overlapping in time domain.
Case2: UE1 with typeA (7symbols) and UE2 with typeB (3 symbols), partial overlapping in time domain (example shown as in slide 8)

## Slide 11
Observation
In case1, although all PUSCH symbols of UE1 fully suffer from the interference of UE2, but the interference correlation matrix can be acquired by DMRS symbol.
In case2, although half PUSCH symbols suffer from the interference of UE2, but DMRS is not polluted, thus the estimated interference correlation matrix is nearly white noise, due to interference mismatch the performance degrades significantly.
Observation：In our view, in real deployment scenarios such issues will happen more often, especially due to flexible configuration in NR. Mechanism to address interference estimation mismatch should be considered.

## Slide 12
THANK
YOU