## Slide 1
Views on NR URLLC/IIOT enhancements in Rel-17
3GPP TSG-RAN WG Meeting #86
Sitges, Spain, Dec 9th-12th, 2019
RP-192544

## Slide 2
NR URLLC/IIOT enhancements– Background
  Basic URLLC features in Rel-15
    Low latency
      “mini-slot” based design for low latency
      low latency and multiple scheduling requests
      UL Configured grant
      UE processing capability#2
    High reliability: “URLLC specific” MCS table in DL and UL
    Inter-UE eMBB&URLLC multiplexing: DL preemption, CBG…
  Enhanced URLLC/IIOT features provided in Rel-16
    Lower latency
      Multiple HARQ-ACK within a slot
    Higher reliability
      Compact DCI, Increased PDCCH monitoring capability, “mini-slot” based PUSCH repetition, enhanced PDCP duplication, multi-TRP based PDSCH…
    Enhanced intra-UE eMBB&URLLC multiplexing
      Two HARQ-ACK codebooks, multiple active configured grant, intra-UE prioritization of UL data/control
    Enhanced Inter-UE eMBB&URLLC multiplexing
      UL cancelation indication, enhanced UL power control
    Enhanced support of time-Sensitive Communications
      Ethernet header compression, DL SPS enhancements, e.g. shorter periodicity, multiple DL SPS…

## Slide 3
Further enhanced URLLC/IIOT - PHY layer aspects
  Further latency reduction
    Specify further improved DL SPS adaptive to the TSN traffic patterns
      DL SPS periodicity shorter than one slot and potential SPS skipping
    Minimize/remove the DL/UL scheduling restrictions for URLLC traffics due to measurement occasions, e.g. measurement gap, SMTC, etc
    Study and specify faster L1 processing timeline, i.e. processing capability #3
  Further reliability enhancements
    PDSCH reliability enhancements for single TRP, e.g. support of mini-slot level PDSCH repetition allowing across slot boundary
    HARQ-ACK feedback enhancements
    Note: the following are to be included in Rel-17 MIMO WID
      Further enhanced multi-TRP operation for reliability
      CSI measurement reporting enhancements for URLLC
  Specify enhanced intra-UE multiplexing of different services
    Intra-UE multiplexing of different services, including UL control and data channels
    Support of efficient out-of-order PDSCH-to-HARQ and PUSCH scheduling
  Study and specify necessary enhancements to enable IIOT/URLLC over unlicensed spectrum, e.g.
    Enhanced FBE channel access, enhanced configured grant/SPS for unlicensed band operation, wideband unlicensed spectrum operation, etc

## Slide 4
Further enhanced URLLC/IIOT - Higher layer aspects
  Further enhanced PDCP duplication
    UE-based PDCP duplication activation/deactivation.
    UE-based leg selection for multi-leg PDCP duplication.
    Dynamic LCP restriction change for PDCP duplication
  Further enhanced Ethernet Header Compression
    The EHC is enhanced to compress more fields in the Ethernet header including the PAD, LENGTH, QTAG and some other fields for certain uses cases (e.g. LLC, SNAP and IEEE 802.1 CB which includes the extra fields of R-TAG, Sequence number and Reserved)

## Slide 5
THANK
YOU