## Slide 1
Views on NR positioning enhancement in Rel-17
3GPP TSG-RAN WG Meeting #86
Sitges, Spain, Dec 9th-12th, 2019
RP-192545

## Slide 2
Views on NR positioning enhancement in Rel-17
  Rel-16 provides the baseline solutions for variable use cases with
    Horizontal accuracy of 3m and vertical accuracy of 3m for 80% of indoor UEs
    Horizontal accuracy of 10m and vertical accuracy of 3m for 80% of outdoor UEs
  Further enhancement of positioning is motivated by new scenarios
    Rather than directly by gaps toward the requirement defined in TS 22.261
  New scenarios at least include the following:
    Positioning for wearables
    Positioning for V2V, V2P and autonomous driving
    Positioning for I-IoT scenarios

## Slide 3
Views on NR positioning enhancement in Rel-17
  Positioning enhancements for wearables
    Power consumption is further optimized;
    Specify idle and inactive positioning:
      Both DL and UL based positioning should be considered;
      The following mechanism could be considered
        Broadcasting the assistance data in idle and inactive mode
        Performing and reporting positioning measurement in idle and inactive mode
        Continue to transmit dedicated UL resource (e.g. SRS) in idle/inactive mode
  Positioning enhancements for V2V, V2P and autonomous driving
    Relative positioning accuracy is of more importance,
      Targeting sub-meter requirements defined in TR 22.186;
      Considering all of in/partial/out coverage cases;
    Power consumption is considered for pedestrian UEs;
    Specify sidelink based and sidelink assisted positioning;

## Slide 4
Views on NR positioning enhancement in Rel-17
  Positioning enhancements for IIoT scenarios
    Specify PRS on unlicensed spectrum;
    Study the potential techniques to further improve accuracy and latency to satisfy the requirement defined in 22.804;

## Slide 5
THANK
YOU