## Slide 1
Views on MR-DC enhancements in Rel-17
RP-192550
3GPP TSG-RAN WG Meeting #86
Sitges, Spain, Dec 9th-12th, 2019

## Slide 2
CA/DC enhancement
  Support of further fast Scell activation
    Scell and SCG keeping during RRC reestablishment
    UE based early measurement, e.g., based on data volume in UE buffer
    Support MAC CE activated or DCI triggered multiple TRS during Scell activation procedure to facilitate Scell activation procedure
      Applies for both FR1 and FR2;
  Support of SCG suspension
    CSI report for SCG is not needed
  Further enhancement for fast MCG recovery
    Fast PCell recovery via Scell
    MCG failure recovery improvement to support more failure types

## Slide 3
Mobility enhancement
  Support of conditional PSCell change/addition
    In Rel-16, only intra-SN without MN involvement may be specified. Other use cases can be discussed in rel-17
  Support mobility enhancement mechanism for FR2 in Rel-17
    Handover interruption is more severe in FR2.
    Thus, how to reduce the interruption time in FR2 handover will be a critical issue.
  Combine condition HO with DAPS, if time is allowed
    The DAPS handover is introduced to reduce the user data interruption, while the conditional HO is supported to improve the handover robustness.
    In order to achieve the high reliability of handover, combination of DAPS and CHO can be considered in Rel-17 if time is allowed.

## Slide 4
THANK
YOU