## Slide 1: Summary of Phase 2 email discussion on NR coverage enhancement
China Telecom
December 2019
3GPP TSG RAN Meeting #86
Sitges, Spain, December 9 – 12, 2019
Agenda: 9.1.1

## Slide 2: Email discussion on NR coverage enhancement
In RAN#84, NR coverage enhancement was identified as one RAN work area for Rel-17 and RAN level email discussion was assigned with the following guidelines:
  Clarify requirements for all relevant deployment scenarios focusing on extreme coverage (not including LPWA). Data rate target FFS.
  Start from Rel-16 email discussion outcome
  Include both indoor as well as wide area

## Slide 3: Email discussion on NR coverage enhancement
The email discussion comprises two phases:
  Phase 1 (till RAN#85): Further clarify the requirement and deployment scenarios starting from initial email discussion in Rel-16 and outcome of link budget evaluation for ITU submission.
  Phase 2 (from RAN#85 to RAN#86): Scope out the objectives for the SID or WID.
  During Phase 1 email discussion, 41 companies including 18 operators shared their views on scenarios, services and channels for coverage enhancement.

## Slide 4: Email discussion on NR coverage enhancement
Phase 2 email discussion comprises two sub-phases:
  Phase 2-1 (till 11/8): Confirmation of the summary of Phase 1 email discussion; and discussion on potential enhanced solutions.
  Phase 2-2 (from 11/14 to 11/28): Scope out the objectives for the SID or WID.
  During Phase 2-1 email discussion
  28 companies including 8 operators provided further views on scenarios, services and channels for coverage enhancement.
  27 companies shared views on potential enhanced solutions.
During Phase 2-2 email discussion
  13 companies provided views on the objectives for the SID

## Slide 5: Conclusions for FR1
Proposal 1: Urban scenario (outdoor to indoor UEs), rural scenario (including extreme long distance rural scenario, e.g. ISD=30km), and LTE/NR co-existence (DSS) scenario, should be taken into account for coverage enhancement for FR1.
Proposal 2: VoIP and eMBB service should be taken into account for coverage enhancement for FR1.
Proposal 3: For urban scenario (outdoor to indoor UEs), the target data rate for UL eMBB is 1 Mbps; and the target data rate for DL eMBB is 10Mbps. For rural scenario, the target data rate for UL eMBB is 100 Kbps; and the target data rate for DL eMBB is 1Mbps.
Proposal 4: Both DL and UL can be taken into account for coverage enhancement for FR1. And coverage enhancement for UL (including PUSCH and PUCCH), should be prioritized.

## Slide 6: Conclusions for FR2
Proposal 5: Indoor scenario (indoor to indoor UEs) and urban/suburban (including outdoor to outdoor UEs and outdoor to indoor UEs) scenario should be taken into account for coverage enhancement for FR2.
Proposal 6: eMBB service should be taken into account for coverage enhancement for FR2. VoIP is considered as second priority for coverage enhancement for FR2.
Proposal 7: For indoor (indoor to indoor UEs) scenario, the target data rate for UL eMBB is 5 Mbps; and the target data rate for DL eMBB is 25Mbps. For urban (including outdoor to outdoor UEs and outdoor to indoor UEs), the target data rate for UL eMBB is [5Mbps]; and the target data rate for DL eMBB is [25Mbps]. For suburban (including outdoor to outdoor UEs and outdoor to indoor UEs), the target data rate for UL eMBB is [50kbps]; and the target data rate for DL eMBB is [1Mbps].
Proposal 8: Both DL and UL should be taken into account for coverage enhancement for FR2. Which channels should be considered depends on evaluation results.

## Slide 7: Potential enhanced solutions for PUSCH
Potential enhance solutions |  | Companies
Time domain | Enhanced repetition, e.g. increased number of repetition Msg3 repetition Enhanced repetition mechanism to overcome frequent cancellation of the repetition due to DL/UL collision for TDD Early termination of PUSCH repetition Finer retransmission, e.g. More RVs | Companies (13) : ZTE, OPPO, CATT, CTC, xiaomi, HW/HiSi, CMCC, Dish, Intel, Verizon, Spreadtrum, vivo
Frequency domain | Enhanced frequency hopping, e.g.inter/intra-slot hopping with more frequency positions Frequency selective diversity, e.g. comb-like Intra-PUSCH hopping, e.g. finer granularity in time domain for one PUSCH Sub-PRB transmission, e.g. half PRB | Companies (11) : ZTE, OPPO, CTC, xiaomi, HW/HiSi, CMCC, Dish, Verizon, Spreadtrum, vivo
DM-RS enhancement | Multi/cross-slot channel estimation Overhead reduction, e.g. DM-RS less slot Increased DMRS density | Companies (11) : ZTE, OPPO, CATT, CTC, CMCC, Dish, Intel, Verizon, Spreadtrum, Samsung, vivo

## Slide 8: Potential enhanced solutions for PUSCH
Potential enhance solutions |  | Companies
Spatial domain | Transmit diversity UL beam management Multiple-panel beam management | Companies (8) : CATT, HW/HiSi, Intel, Spreadtrum, AT&T, Intel, vivo
Code domain | Spreading w/ CDM, e.g. PUCCH-like PUSCH | Companies (3) : ZTE, Dish, vivo
Power domain | Enhancement of power control Higher power UE for FDD PSD boosting | Companies (4) : ZTE, HW/HiSi, Intel
Packet aggregation | Aggregate multiple RTP packets into one RTP packet | Companies (2) : CTC, vivo
Enhancement on pi/2 BPSK waveform |  | Companies (6) : IITH, IITM, CEWIT, Tejas Networks, Reliance Jio, Saankhya Labs
Low PAPR scheme (e.g. pi/4 BPSK) |  | Companies (1) : ZTE
Support of URLLC MCS table for eMBB |  | Companies (1) : ZTE
SUL based solutions |  | Companies (2) : HW/HiSi
Uplink forwarding (e.g. relay) |  | Companies (2) : HW/HiSi

## Slide 9: Potential enhanced solutions for PUCCH
6 companies thought some enhancement approaches for PUSCH enhancement can be applied to PUCCH.
4 companies thought enhancement on PUCCH repetition should be considered.
1 company thought Uplink beam management and multi-panel beam management should be considered.
8 companies thought the discussion on the candidate enhanced solutions can be part of SI/WI.
1 company proposed sequence-based PUCCH with non-coherent detection.

## Slide 10: Potential enhanced solutions for other UL channels
7 companies thought SRS should be enhanced.
2 companies thought PRACH needs to be enhanced.
5 companies thought it depends on evaluations.
2 companies thought the discussion on the candidate enhanced solutions can be part of SI/WI.

## Slide 11: Potential enhanced solutions for other DL
10 companies thought PDCCH needs to be enhanced; PDCCH repetitions may be a potential solution.
3 companies thought coverage for DSS needs to be studied and enhanced.
10 companies thought broadcast signals/channels needs to be enhanced.
8 companies thought PDSCH needs to be enhanced.
6 companies thought that all channels must work at SINR of -12 dB with acceptable synchronization performance and BLER performance to enhance large cell coverage of the order of 12 km ISD or more.
3 companies thought the discussion on the candidate enhanced solutions can be part of SI/WI.

## Slide 12: SID on NR coverage enhancement
The objective of this study item is to study potential coverage enhancement solutions for specific scenarios for both FR1 and FR2. The detailed objectives are as follows.
The target scenarios and services include
  Urban (outdoor gNB serving indoor UEs) scenario, rural scenario (including extreme long distance rural scenario) and LTE/NR co-existence (DSS) for FR1
  Indoor scenario (indoor gNB serving indoor UEs) and urban/suburban scenario (including outdoor gNB serving outdoor UEs and outdoor gNB serving indoor UEs) for FR2.
  TDD and FDD for FR1.
  VoIP and eMBB service for FR1.
  eMBB service as first priority and VoIP as second priority for FR2.
Identify baseline coverage performance for the above scenarios and services based on link-level simulation
  UL channels (including PUSCH and PUCCH) are prioritized for FR1.
  Both DL and UL channels for FR2.

## Slide 13: SID on NR coverage enhancement
Study the potential solutions for coverage enhancements for the above scenarios and services
  The target channels include at least PUSCH/PUCCH for scenarios.
    Study enhanced solutions, including time domain/frequency domain/DM-RS enhancement; other solutions are not precluded.
  Study enhanced solutions for PDCCH for LTE/NR co-existence (DSS).
  Evaluate the performance of the potential solutions based on link level simulation.
Study the coverage performance and additional enhanced solutions for the above scenarios and services for FR2
  Identify the target channels for coverage enhancement based on the above evaluation.
  Study the specific potential solutions for the target channels.
  Evaluate the performance of the potential solutions based on link level simulation.

## Slide 14
Thank you！