## Slide 1
Support Air-To-Ground in NR
CMCC, ZTE
3GPP TSG RAN Meeting #86 RP-192598
Sitges, Spain, December 9-12, 2019
Agenda Item: 9.1.1

## Slide 2: Deployment scenario for ATG
Scenario: to provide broadband access for civil aircrafts
  ATG gNB deployed on the ground, with antennas pointing upward to form an aerial cell
  Aircraft as a special UE
  Aircraft to ATG gNB: 5G air interface
  Aircraft to passengers: WiFi access
Extreme large ISD & coverage range
Frame structure with large periodicity in TDD
Interference between ATG & terrestrial
Mutual interference between ATG and terrestrial networks if the same frequency is used
Powerful ATG terminal capability
Higher EIRP
High stability LO (local oscillator)
Location information can be gor via GNSS
Typical ISD is 100~200km to control the cost of network deployment
Up to 300km coverage range to cover planes above the sea with gNB on shore
E.g., 20 ms TDD UL-DL switching periodicity in order to limit the GP overhead

## Slide 3: Comparison of deployment scenario between NTN and ATG
 | NTN | ATG | Comments
Access scenario | gNB in space, and UE on ground | gNB on ground, and UE in sky | Generally, ATG can be seen as inversely deployed NTN
gNB characteristic |  | Altitude: 40m Speed: 0 Antenna: point to sky Max coverage : 100 ~ 300km | w.r.t. gNB, NTN is much more complex than ATG
UE characteristic | Altitude: aircraft (10km), others (3m) Speed: aircraft (1000km/h), others (3km/h) UE w/ or w/o directional antenna UE w/ or w/o location determination capability (e.g. GNSS): both supported | Altitude: 6~12km Speed: ~300m/s UE w/ directional antenna UE w/ high stability LO UE knows location | w.r.t UE, both w/ similar max altitude & speed
Others | FDD is typical, and TDD is also considered for HAPS and LEO Dedicated frequency, not shared with terrestrial network | TDD should be supported Frequency sharing with terrestrial network | Common enhancements w.r.t the TDD can be used for ATG
 | LEO | GEO
Altitude | 500~2000km | 35786km
Speed | 7.5km/s | 0
Antenna | point to the earth with multiple spot beams | 
Max cell size | 200km | 1000km

## Slide 4: Comparison of deployment scenario between NTN and ATG
    Summary: ATG can be seen as an inversely deployed network of NTN, and they share several common technique challenges, e.g., large cell coverage range, high doppler shift, which will not introduce too much additional work in NTN.
    To do: ATG compatible solution could be specified in NTN WID

## Slide 5: Challenges and Potential Enhancements for ATG
Aspect | Potential problem | Potential enhancement
Extreme large cell coverage range (e.g., up to 300 km) and high speed (e.g., up to 1200km/h) | Current spec can support up to 100km coverage range and up to 500km/h. | PRACH format enhancement. Enhancements on UL time and frequency synchronization
TDD UL-DL Config. with >16 DL slots (e.g., 28DL:4GP:8UL with 30kHz SCS ) | Limited HARQ process number (16) Limited K1 range (0~15) for PDSCH-to-ACK feedback | Support >16 HARQ process for PDSCH or TTI bundling with larger TBS Support larger value range for K1 (e.g., 0~31)
Aspect | Potential problem | Potential enhancement
Coexistence between ATG and terrestrial network | Core specifications of RF and RRM requirements for coexistence Co-existence evaluation for ATG network (e.g. ACLR, ACS) Study and identify new power class UE/BS category for ATG network Study and identify RF requirements for ATG UE/BS Study and identify RRM core requirements | 
RAN1 Part:
RAN4 Part:

## Slide 6: Discussion on feasibility of reusing NTN solutions in ATG
Challenge in ATG | Potential enhancement | Related NTN solutions | Whether can be used in ATG
Extreme large cell coverage range (e.g., up to 300 km) and high speed (e.g., up to 1200km/h) | PRACH format enhancement | [Agreed to be supported] Enhancement on PRACH formats and/or preamble sequences | Yes
 | TA related enhancement | [Agreed to be supported] TA compensation (e.g., autonomous acquired TA or Indicated common TA ) | Yes, but full TA compensation at UE side is preferred to maintain the DL/UL frame timing alignment at network side to support TDD network rather than to support FDD network only
TDD UL-DL Config. with >16 DL slots | Support >16 HARQ process for PDSCH | [Discussed w/o convergence] >16 HARQ process with 4-bit HARQ process ID field kept in DCI | Yes, if supported in NTN WI
 | Support TTI bundling with bigger TBS | Not involved | No, but it is no needed if >16 HARQ process is supported
 | Support larger value range for K1 (e.g., 0~31) | [to be further discussed in WI] Extending the range K1 and/or K2 beyond R15 | Yes, if supported in NTN WI
Coexistence between ATG & terrestrial | Core specifications of RF and RRM requirements | Not involved | No, core specifications of RF and RRM requirements is necessary in RAN4

## Slide 7: Recommendations for ATG compatible solutions in NTN
Specify features to support extreme large coverage (up to 300km) and TDD frame with >16 DL slots, including the following aspects [RAN1]
  Potential enhancements to support UL time and frequency synchronization
    Note: Solution for NTN to guarantee DL/UL frame timing alignment at network side is preferred to support TDD network
  Potential enhancements on PRACH formats and/or preamble sequences
    Note: Suggest to be specified in NTN WI (No additional efforts for ATG)
  Potential enhancements to support >16 HARQ processes for PDSCH
    Note: Suggest to be specified in NTN WI
  Potential enhancements to support larger value range for PDSCH-to-HARQ feedback timing (K1), e.g., 0~31
    Note: Suggest to be specified in NTN WI
  Proposal: ATG compatible physical layer solution could be specified in NTN WID
Core specifications of RF and RRM requirements for coexistence between ATG and terrestrial network [RAN4]
  Co-existence evaluation for ATG network (e.g. ACLR, ACS)
  Study and identify new power class UE/BS category for ATG network
  Study and identify RF requirements for ATG UE/BS
  Study and identify RRM core requirements
  Proposal: A separate ATG WI led by RAN4 could be considered if the RAN1 part is specified in NTN WI

## Slide 8
Thank you!