## Slide 1
3GPP TSG RAN meeting #86
Sitges, Spain, December 9-12, 2019
Agenda item: 9.3.5
RP-192606
Motivation on support of LMC in NG-RAN for local NR positioning
CMCC

## Slide 2
Benefits of introducing LMC in NG-RAN
Observation 1: NR positioning architecture in Rel-15 cannot fully satisfy the requirements of operators, LMC in NG-RAN has many benefits.
    Reduced latency: As studied in SA2, the number of signaling interfaces to support location services can drop significantly and latency performance of the location service can be greatly improved as the signaling transmission process via 5GC can be avoided
    Address the security concerns of vertical domain: Positioning data will not be exposed outside the private network, which satisfy the requirement of vertical domains
    Easier deployment: A location server functionality in RAN would allow operators to flexibly complement the operation of 5GC LMF based on e.g. the QoS requirements of the location service.
    Enable efficient network optimization: It allows RAN to have UE locations to complement MDT and enable better beamforming, and indoor/outdoor classification, etc.
    Better scalability: A distributed location server functionality would better scale in case a large number of UEs need to be supported (e.g., IoT use cases).

## Slide 3
    To address low latency and high performing positioning requirement, SA2 has studied solutions 15, 23, 26, 28 and acknowledged the benefits of introducing local LMF (i.e., LMC) in NG-RAN
    SA2 made the following conclusion
      NG-RAN node enhanced with the support of location management functionality may be selected to perform UE positioning locally in the RAN under the condition that RAN WG(s) concludes that NG-RAN supports location management functionality.
Status quo of SA2
Observation 2: SA2 has already studied the local LMC in NG-RAN and acknowledged the benefits of introducing this architecture.

## Slide 4
    RAN2:
    RAN2 has also carefully analyzed the pros and cons of the architecture “local location management function in NG-RAN”, and finally recommended to normative work.
    From RAN2 perspective, we conclude that this option is recommended for normative work, provided the concerns raised in the study phase are addressed
    RAN3:
    RAN3 cannot make recommendations due to lack of the time to study the architecture and specification impact, so a new SI is approved at RAN #83 meeting.
Status quo of RAN in the preceding positioning SI
Observation 3: RAN2 has already studied and recommended to support LMC in RAN for NR positioning in Rel-16.
Observation 4: RAN3 could not make recommendations just because of no studies on the architecture and specification impact.

## Slide 5
    RAN3 has finished the SI with the following conclusions
RAN3 has studied the feasibility and specification impact of local LMF (i.e., LMC) in NG-RAN.
Three architecture alternatives have been studied. It is concluded that support of LMC in NG-RAN is feasible
Architecture 3 seems like the most promising option among the ones studied. RAN3 did not evaluate the benefits of any of the architecture options in terms of latency towards the core network, RAN3 also did not fully evaluate, e.g., mobility issues associated with the introduction of the LMC.
RAN3 could not reach consensus on any recommendation for normative work.
Progress of local NR positioning in NG-RAN SI

## Slide 6
  Further observations
    It seems only two companies have concerns on the recommendation of normative work
    RAN3 is not the right group to address the first concerns, the benefits in terms of latency has been acknowledged by SA2 and benefits of deployment flexibility are further clarified by the operators in RAN3
    The proponent of the recommendation for normative work did not see the issue with mobility. Since LMC in NG-RAN is mostly to satisfy local positioning requirement, it is still promising in scenarios without mobility.
Progress of local NR positioning in NG-RAN SI
Observation 5: RAN3 has studied the feasibility and specification impact of LMC in NG-RAN and confirmed the feasibility.
Observation 6: RAN3 has performed the down-selection of the architecture alternatives
Observation 7: Concerns on mobility issues can be addressed by supporting LMC in NG-RAN without mobility first.

## Slide 7
Summary
Proposal: Recommend to proceed with normative work for LMC support in NG-RAN