## Slide 1: Motivation for Introducing DL 1024QAM in NR FR1
Ericsson
3GPP TSG-RAN Meeting #86
Sitges, Spain, December 9-12, 2019
Agenda item: 9.1.1
RP-192612

## Slide 2: Motivation
Rel-15 NR supports downlink modulation order up to 256QAM for PDSCH.
LTE has introduced even higher order modulation order of 1024QAM for PDSCH in Rel-15.
NR should be competitive to LTE with regard to the spectral efficiency especially on refarmed operating bands and mid-bands, i.e., FR1
Even for NR, high SNR conditions supporting DL 1024QAM can be achievable in FR1 with:
  Small cell / indoor cell / non-sectorized cells
  Beamforming (in mid-bands 3-6 GHz)
It is expected that meeting EVM and demodulation requirements in the FR1 range should be the same as LTE from an implementation perspective and feasible.

## Slide 3: Summary of objectives
Specify high order modulation for PDSCH [RAN1]
  Specify 1024QAM constellation as specified in E-UTRA for DL PDSCH
  Specify corresponding MCS table
  Specify corresponding CQI feedback
Define RRC signaling and UE capabilities [RAN2, RAN1]
Introduce corresponding RF requirements to support DL 1024QAM in FR1 [RAN4]
Specify the necessary UE performance requirements [RAN4]