## Slide 1: Views on UE specific DRX for NB-IoT
Sequans Communications
December 2019
RP-192663
3GPP TSG RAN Meeting #86
Sitges, Spain, December 9-12, 2019
Document for: Approval

## Slide 2: Background - UE specific DRX for NB-IoT
Q3
  RAN2#107
    CRs (removing restrictions in NB-IoT), not agreed due to concerns from companies
  RAN#85
    WID updated with new objective to introduce UE specific DRX for NB-IoT, based on the assumption that only removal of corresponding restriction is needed (RP-191828)
    LS sent to SA2/CT1 (action: align their specifications in coordination with RAN2)
Q4
  RAN2#107bis (~1h discussion)
    Not agreed due to concerns (i.e. not backward compatible, if one of UE or NW does not support, paging is broken)
    Agreement “Will wait for progress from SA2/CT1”
  SA2#135
    A CR was agreed for 5GS (signal separately NB-IoT UE specific DRX)
  RAN2#108 (no discussion)
    [108#98][NB-IoT] UE specific DRX (Huawei) Scope: Pending LS from SA2, progress on the details / Intended outcome: Report, including TP for stage 3 if possible.
  SA2#136
    Different views on using separate/common UE specific DRX at NAS level, summarized in Reply LS RP-192393 .
      RAN WG3 was added to the To: line
Notes:     WID updated with new objective to introduce UE specific DRX
      based on the assumptions from RP-191828 that UE specific DRX can be easily supported for NB-IoT by removing corresponding restrictions in specifications without introducing new mechanism and despite concerns on impact on reflector

## Slide 3: Additional concern 1 – Multiplexing with bad coverage Ues Long paging latency despite short UE specific DRX configuration
NB-IoT system was designed for delay tolerant traffic
  Fast reachability is a complete new use case for NB-IoT
The eNB shall be able to schedule timely UEs using UE specific DRX, so that the feature is useful and the increased UE power consumption is not wasted
Timely addressing of UEs (in good coverage) multiplexed with UEs in bad coverage is an issue in NB-IoT, addressed from Rel-13 with DL scheduling gaps (reserved for addressing UEs in good coverage). But in IDLE, all UEs use same Rmax i.e. would be considered in “bad coverage”.
No such problem in LTE
No such problem in eMTC
  Much more limited number of repetitions, MPDSCH can be scheduled on different NB, etc (DL scheduling gaps were never required in the first place).
If this happens, the feature
is useless
Increases UE power consumption for no gain
DL scheduling gaps increase the problem

## Slide 4: Additional concern 2 – CN / eNB lack of coordination CN may not know the used paging cycle
The CN is supposed to know the DRX cycle used to page a UE, to adapt its paging strategy. Currently the default paging value is sent to the MME / AMF
This signaling would become moot if the CN does not know whether eNB will use UE specific DRX or not
  Because e.g. not supported or not configured (e.g. if lot of UEs in deep coverage in the cell)
For LTE/eMTC, no such issue as UE specific DRX is mandatorily supported by eNB/UE
  The CN can always derive the used Paging Cycle
Hence signaling from eNB to MME / AMF might be required
  I.e. RAN3 impact (currently excluded from the WID)
This impact was not yet discussed

## Slide 5: Additional concern 3 – Paging overlap / fractional nB value
For eMTC and NB-IoT, extended nB values (e.g. T/256, T/512, …) were introduced to space out POs (every 256 RFs, every 512 RFs etc) so that enough repetitions could be sent.
However, this makes it possible to have fractional nB values as T might be such that nB<1 (which was not possible in legacy).
It has following drawbacks (mostly shared by companies as captured in R2-1901523)
  Possible paging CSS overlap (not enough repetitions can be sent between 2 POs)
  Wrong distribution of UEs on paging carriers, e.g. if 2 carriers with same weight, UEs will use only 1 carrier
    This is because paging formulas for POs/paging carriers were never assuming nB<1.
Discussed for eMTC during ~6 months, with the following conclusion capture in CM notes:
  RAN2 understands that nB value can be fractional. It is up to the network to ensure that number of valid subframes configured would make it possible to transmit enough number of repetitions to transmit PDCCH scrambled with P-RNTI between POs for the maximum CE level supported in the serving cell.
For eMTC, acceptable because CSS overlap is only when a few valid subframes are configured
For NB-IoT, applying UE specific DRX means the following (even if ALL subframes are valid):
  Rmax=2048 can no longer be configured (even for 1.28s, the longest UE specific DRX value, the POs would overlap)
  If even lower DRX cycle is agreed (e.g. 320ms): Rmax= 512, 1024 can no longer be configured

## Slide 6: Possible simple solutions
Concern 1: (R2-1916236)
  Allow mapping of UEs using UE specific DRX to separate carriers
  Limit minimum paging cycle that can be used in a cell (e.g. by SIB broadcast)
Concern 2: (R2-1916235)
  Add RAN3 to WI
    To include necessary signaling from eNB to CN so that CN is aware of used paging cycle
Concern 3:
  Modify paging formula for UEs using UE specific DRX
    Ensure nB>=1 (avoid carrier load balancing issues)
  Specify intended behavior in case of PO overlap
    E.g., UE should re-negociate UE specific DRX so that this case does not happen
  (solutions were already discussed for eMTC)

## Slide 7: Conclusion
There are still concerns to be addressed before the feature can be deemed usable
  Long paging latency despite short UE specific DRX configuration
  MME / eNB lack of coordination
  Paging overlap / fractional nB value
Solving the backward compatibility issue (down selection from RP-192393 options) is a necessary but not sufficient step.
  There are already solutions on the table

## Slide 8: Proposals
Revise the WID to include RAN3 responsibility.
  proposed WID revision in RP-192664
Pursue solutions for all identified additional concerns 1-3 for UE specific DRX for NB-IoT
Reconfirm target completion of work in Rel-16.
  Push back to Rel-17 can be discussed in RAN#87, if needed