## Slide 1: Adding new objective in NR RRM enhancement WI
MediaTek Inc.
3GPP TSG RAN#86 RP-192666
Sitges, Spain – December 9th-12th, 2019 Agenda Item 9.4.25

## Slide 2: Background
TCI-state switch requirements are defined in TS38.133 §8.10
  Only a subset of the functionality defined in RAN1 and RAN2 specifications is covered in RAN4
RAN1/RAN2 coverage: Functionalities with TCI-state switch and UL spatial relation switch | RAN4 requirements
PDSCH (DCI, MAC and RRC triggering) | 
PDCCH (MAC and RRC triggering) | 
CSI reporting (DCI, MAC and RRC triggering) | 
PUSCH (DCI) | 
PUCCH (MAC and RRC triggering) | 
SRS (DCI, MAC and RRC triggering) | 

## Slide 3: Consequences
UE performance not guaranteed during TCI-state switch or UL spatial relation switch
Missing requirements for TCI State switch of CSI-RS for CSI Reporting
  Throughput Loss: The network has no expectation on how long the UE should be able to report CSI based on new TCI-state. Without a clear expectation, network can only adopt a conservative MCS in scheduling
Missing requirements for Spatial relation switch for uplink (PUCCH, PUSCH, SRS)
  Latency in beam correspondence: How fast the UE can adjust its UL signals to a new direction in which UE receives SSB or CSI-RS from DL is unpredictable. The risk of failed UL transmission increases

## Slide 4: RAN4 Way Forward: R4-1915937
RAN4#93-approved way forward:

## Slide 5: Proposal
Proposal 1: Add new objectives in R16 NR RRM enhancement WI on TCI state switch of the CSI-RS for CSI reporting and spatial relation switch for uplink
Proposal 2: Increase the TU of R16 NR RRM enhancement WI or rather extend the WI by one more quarter

## Slide 6: Appendix Proposed additional objectives to Rel-16 RRM Enh. WI
TCI state switch of the CSI-RS for CSI reporting
  Study to introduce the delay requirement for TCI state switch of the CSI-RS for CSI reporting
  UE behavior if the TCI-state for CSI reporting is not within the active TCI state list for PDSCH
Spatial relation switch for uplink
  Introduce the delay requirements for spatial relation switch for uplink channels and SRS