## Slide 1: Satellite NB-IoT Technical Focus
MediaTek Inc., Eutelsat, Ligado, Inmarsat, Intelsat, HUGHES Network Systems, Fraunhofer
3GPP TSG RAN#86 RP-192671
Sitges, Spain – December 9th-12th, 2019 Agenda Item 9.1.1

## Slide 2: Satellite NB-IoT Proposal
Simple adaptation to satellite use in LEO and GEO
  Preserving NB-IoT cost & energy efficiency
No need to disable HARQ
  Legacy HARQ scheduling delay can accommodate delay
  Latency is not an issue for delay-tolerant IoT applications
Simpler operations with NB-IoT in connected mode
  No HO, No CSI
Low data rate, high latency, intermittent packet transmission
  No issue for RLC and PDCP operations
Can also be deployed inband an NR carrier
  see RP-190846 – Rel-16 NB-IoT WID
Very limited specification impact
  New PRACH format/sequence for initial cell access without pre-compensation of timing and frequency offset (LEO)
    Re-use rel-13 RACH w/ fractional frequency offset and cover code robust to satellite for RTD and frequency offset
    Residual FO estimation for UL frequency correction indication in Msg2
  Timing relationship and UL time synchronization enhancements (LEO, GEO)
    Initial TA, TAC, extension of RAR window
    Timing offset for RAR window, Msg3, data, UL HARQ feedback, MAC CE, DRX and SR timers
  Beam/Cell re-selection by idle UE (LEO)
    Enhanced RLF trigger
    Satellite-assisted SI - list of next beams, mapping of PCI, satellite/beam-specific parameters
  RRM/RF performance requirements [RAN4]

## Slide 3: Notes Leverage of NTN NR SI Recommendations
The following NR NTN SI RAN1 recommendations have synergies with NB-IoT [R1-1913436]
  Class 3 UE can be served by LEO and GEO in FR1 with appropriate beam layout (including potential frequency reuse and/or polarization re-use)
  Other UE (e.g. VSAT and phase array) with high TX/RX antenna gains can also be served by GEO
  To address the identified issues due to long propagation delays (LEO, GEO), large Doppler effects and moving cells (LEO) for a potential normative phase, it is proposed to focus on the following:
    Timing relationship enhancements
    Enhancements on UL time and frequency synchronization
    Enhancement on the PRACH sequence and/or format in the case pre-compensation of timing and frequency offset is not done at UE side
The following NR NTN SI RAN2 recommendations have synergies with NB-IoT [R2-1916396]
  Idle mode:
    Use of satellite Ephemeris information and/or UE location information
    Use earth-fixed tracking area to avoid frequent TAU
    NTN cell specific information in SIB
  Connected mode:
    Compensation for propagation delay differences in the UE measurement window between cells originating from different satellites
    Enhancements to measurement configuration and reporting,
    Assisted cell selection/reselection to address LEO/Earth moving cell solutions