## Slide 1: Views on Rel-17 NR Positioning enhancements
Ericsson
3GPP TSG RAN#86
Sitges, Spain
December 9th -12th 2019
Agenda Item: 9.1.2
RP - 192676

## Slide 2: Scope of the WID
Objective 3 and 4 (positioning enhancements for commercial use cases /IIOT use cases and positioning for V2X) are worded as to include a study prior to normative work.
Observation: Given the large scope of these objective, a study item phase should be a precondition to proceeding to work item phase
Proposal: split the current draft WID between a SI and WI so that each of the objective can be validated prior to normative work start.
  SI can include:
    study RSTD measurements in RRC idle/inactive state and its potential benefits (objective 1)
    Define additional scenarios for IIOT /V2X (steps 3.a and 4a in the draft WID)
    Evaluate the performance for IIoT with rel16 positioning solution (step 3.b in the draft WID)
    Evaluate the candidate enhancements to meet the new requirements. The candidates are the ones listed in step 3.c/3.d and 4.b/4.c for IIOT and V2X, respectively.

## Slide 3: RRC idle/inactive state objective
Our understanding of the objective is to study whether RSTD measurements can be performed in idle/inactive state.
The study scope, should be clarified
Proposal reword objective 1 in the WID as
  study, and if benefits are identified, specify measurements in RRC idle/inactive state and the benefits associated with this.

## Slide 4: LMF in the RAN and coordination between LMC in RAN and 5GC entities
RAN3 has studied the feasibility and specification impact of local LMF (i.e., LMC) in NG-RAN, however:
  RAN3 did not evaluate the benefits of any of the architecture options in terms of latency towards the core network
  RAN3 also did not fully evaluate, e.g., mobility issues associated with the introduction of the LMC
  NG-RAN acting as local client (LCS) was not treated
  It is explicitely mentioned in the SI outcome that RAN3 did not reach any consensus and no recommendation is currently available for normative work.
Proposal: Since the above points hardly justify a WID, it is proposed to not specify LMF in RAN in Rel-17

## Slide 5: Positioning enh. for commercial /(I)IoT use cases
The objective of the Positioning WI/SI should be to position the UE, The NW calibration and NW synchronization should not be part of Positioning and is outside the scope of standardization
Proposal Remove the “3. C. iv” item NW calibration and NW synchronization from Positioning SI/WI.

## Slide 6: Sidelink interface / V2X positioning
V2X positioning / outdoor IOT cases can reuse exisiting features such as GNSS (potentially with 5G RTK assistance information) or rel-16 RAT based positioning.
proposal: remove objective 3.d and 4 from the WID.

## Slide 7: Rel 17 Positioning Integrity
Rel 15 and 16 has introduced support for RAT indepentent (GNSS RTK) and RAT dependent precise positioning for accuracies well within 1m accuracy
The following contributions and references indicate the need for studies and work on positioning integrity, which has not yet been addressed:
  TR 22.862, “Feasibility Study on New Services and Markets Technology Enablers for Critical Communications”
  RP-191919, ” Views on Rel-17 Positioning Enhancements”, Swift Navigation
  RP-192981, ” Motivation to study integrity in the position domain”, ESA
  RP-192750, ” Motivation for Study on Positioning Integrity”, Swift Navigation, Deutsche Telekom

## Slide 8: Rel 17 Positioning Integrity
3GPP Rel 15 and 16 has created an open, global and interoperable specification of OSR and SSR GNSS RTK – the only of its kind
3GPP Rel 16 has also created an open global and interoperable specification of 5G precise positioning
This has potential to create a large eco system that can address very different use cases but also the very specific requirements of specific use cases such as safety critical automotive use cases
Use cases benefitting from precise positioning also requires integrity
Therefore – in order to realize this eco system, positioning integrity is needed in 3GPP
Proposal: Add positioning integrity as study and normative work on identified parts in Rel. 17.