## Slide 1: Agenda Item: 9.1.3 Source: AT&T Title: Proposal for RAN Enhancements for New Deployment Models Document for: Discussion/Decision
3GPP TSG RAN Plenary Meeting #86 RP-192707
Sitges, Es: December 09-12, 2019

## Slide 2: Motivation
In Rel 16, various features such as multi-TRP, CA/DC enhancements have been developed however it is not easily possible to deploy these features since they either require a C-RAN like deployment or an ideal (0 latency) inter-connect between the DUs
In Rel 17, we would like to propose enhancements to RAN interfaces to allow for CU-CU and DU-DU coordination for use cases to take advantage of Rel-16 features
UE
CC1
CC2
CA across gNB
UE
CC1 Lyr1
CC1 Lyr2
Multi-TRP across gNB

## Slide 3: Use Case 1: Inter gNB Multi-TRP
In Rel 16, RAN1 specified various flavors of multi-TRP solutions
Multi-TRP with single DCI: Joint scheduling between 2 TRPs e.g. same MAC between 2 TRPs
Multi-TRP with multi-DCI: Independent scheduling between 2 TRPs with same (or separate) MAC. A solution targeting non-ideal backhaul scenarios
Currently there is no low latency coordination mechanism between two MAC entities and in Rel 17 we propose to develop a mechanism for this MAC-MAC coordination in time-scales as required by the RAN1/RAN2 specifications
DCI1
DCI2
PDSCH 1
PDSCH 2
CU
CU
DU
DU
DU
DU
UE
UE
Inter-DU
M-TRP
Inter-CU
M-TRP
X2
F1

## Slide 4: Use Case 2: Inter gNB CA
Aggregation between pico cell tier and macro cell tier is a very important use case that allows operators to improve network performance in an effective way
Currently the only way to do this is:
Ideal backhaul (e.g. C-RAN)
DC
Both the solution have limitations especially if the aggregation is between FR1 and FR2
CU
CU
DU
DU
DU
DU
UE
UE
Inter DU
CA
Inter CU
CA
X2
F1

## Slide 5: Use Case 3: Traffic Multiplexing
Use cases such as support of different traffic requirements (e.g. eMBB, URLLC) on different DUs with potentially different functional splits is very important to improve the efficiency and performance of different traffic deployments on the network
Enabling such deployments requires coordination between schedulers on different DUs. Such coordination is not currently supported in Rel. 16
CU
DU
DU
F1
F1
MAC
RLC
PHY
RF
MAC
RLC
PHY
RF
New interface
URLLC, eMBB
eMBB

## Slide 6: Latency Tolerance of CA
CA is more sensitive to latency since the PCell and SCell scheduling are more closely tied. However with distributed scheduling it is still possible to get gain with non ideal backhaul.
CA is more sensitive to latency between the DU’s than DC (as expected)
10 + 10 MHz CA
2x2 MIMO
500m ISD
Typical X2 type latency might not be good enough for inter-site CA

## Slide 7: Proposed MAC-MAC Interface
A new logical interface between peer MAC entities at non-co-located gNB-DUs.
This new MAC-MAC interface (Xmac) enables communication of control and user plane information between peer MACs for inter-site coordination
The new interface enables direct MAC-to-MAC coordination between peer DUs that are either under the same CU or under different CUs.
The new interface enables inter-site CA without requiring a centralized MAC and very low latency high throughput transport between DUs.
Unlike DC-based solutions that are limited to aggregation across two sites (MN and SN), inter-site CA solutions via a MAC-MAC interface can be enabled across more than two sites because it is still a CA-based solution, it requires the UEs to transmit only on a single PCell uplink.

## Slide 8: Summary
In Rel 17 architecture and inter-CU and inter-DU coordination techniques must be developed in order to take advantage of some of the RAN1/2 features developed in Rel 16.
Three of the key uses cases to focus on are:
Inter-DU and inter-CU multi DCI multi TRP solution
Inter DU and inter-CU CA
    FR1-FR2 CA
    FR1-FR1 CA
  Inter-DU multiplexing solution for different traffic types