## Slide 1: Agenda Item: 9.1.1 Source: AT&T Title: Key Considerations for MIMO Enhancements in Rel. 17 Document for: Discussion/Decision
3GPP TSG RAN Plenary Meeting #86 RP-192708
Sitges, ES: December 9-12, 2019

## Slide 2: MIMO Enhancements
Rel. 17 enhancement for NR MIMO had the following guidance from the RAN chair in RAN#84 [1]
• Enhancements motivated by current commercial deployments
• Expand use cases
• E.g. Support for cases with high speed mobility, better support for FDD
Accordingly, an email discussion was kicked off in September to collect companies views and draft a WID proposal for RAN#86
RP-192708

## Slide 3: Enhancements for MIMO in Rel. 17
In this document, we focus on two major topics for enhancements for MIMO in Rel. 17
    FDD MIMO Enhancements for FR1
    MIMO Enhancements for FR2
We believe that FR1 and FR2 are both equally important for NR deployment and enhancements targeting both frequency bands should be included in MIMO enhancements in Rel. 17
RP-192708

## Slide 4: FDD MIMO Performance Enhancements
In general, current LTE/NR MIMO feedback considers the angle domain as “long term” component thus designing the DFT beams to trace angles (DoA, AoA, ZoA, ZoD)
Type II CSI codebook in NR Rel. 15/16 improves MIMO performance in FDD bands at the expense of more feedback overhead and higher UE complexity
DFT based compression was introduced for type II CSI in Rel. 16 to reduce the feedback overhead
Improving the performance of MIMO in FDD bands beyond Rel. 15/16 while reducing the feedback overhead is crucial in Rel. 17
RP-192708

## Slide 5: FDD MIMO Performance Enhancements
Unlike TDD, exploiting reciprocity in FDD can be challenging depending on the separation between the UL and DL carriers, and over the air calibration limitations
Commonality between the UL and DL channels in FDD is conducive to using FDD reciprocity techniques
Partial FDD reciprocity can be exploited to improve the DL spectral efficiency
Mean reciprocity up to 3.5 dB for FDD
DL
UL
1.9GHz
280MHz
RP-192708

## Slide 6
FDD MIMO Performance Enhancements
Exploring the power-delay and power-Doppler profiles to track long term and frequency domain changing trends can significantly improve the feedback overhead
Exploit the invariance and sparsity of the channel in the delay Doppler domain
Extract reciprocity or partial reciprocity (channel covariance) based on delay-Doppler plane invariance
Need for UE-assisted over the air calibration for FDD
Study CSI measurement and reporting (including codebook) where angle(s), Doppler(s) and delay(s) are estimated at the gNB based on SRS, and the remaining DL CSI is reported by the UE along with possible UE-assisted calibration mechanism, mainly targeting FR1
gNB
UE
Channel
Calib/Feedback Container
Unlike TDD Reciprocity, FDD Reciprocity requires UE assistance for calibration
SFFT
ISFFT
Channel in delay Doppler domain exhibits more sparsity and invariance
RP-192708

## Slide 7
FDD MIMO Performance Enhancements
Feedback enhancements based on exploring the channel variations over time (Doppler) and frequency (delay) are beneficial for feedback overhead reduction, especially in high mobility scenarios
CSI-RS design in the delay Doppler domain: CSI-RS may be overlaid with data REs in the time-frequency domain
Feedback overhead reduction through adaptive feedback and grid subsampling in the delay-Doppler domain
Study reporting mechanism(s) for CSI overhead reduction and for tackling CSI aging assuming high speed UEs
SFFT
ISFFT
Time domain
Frequency domain
Doppler domain
Delay domain
Time frequency grid
Delay Doppler grid
RP-192708

## Slide 8: MIMO Enhancements for FR2
Enhancing MIMO operation in FR2 should be one of the main objectives of the Rel. 17 MIMO WI. Though some improvements were made in Rel. 16 on beam management and multi-TRP, more work is needed to:
Facilitate more efficient DL/UL beam management with lower latency and overhead
Facilitate beam selection and simultaneous uplink transmission for UEs with multiple panels
Facilitate multi-TRP operation through multi-panel reception and transmission
RP-192708

## Slide 9: Multi-Beam/Panel Enhancements
Multi Beam/Panel Enhancements to improve reliability and robustness and reduce the overhead of the beam management procedure in NR are required in Rel. 17.
Use cases such as IAB, URLLC, and V2X could benefit from multi-beam and multi-panel improvements
Specify features to streamline the beam management procedure on the DL/UL with multi-beam efficiency enhancements to decrease latency and overhead
Specify multi-beam enhancements to enable multi-TRP operation in FR2
Specify better interworking between beam failure recovery procedure and RLM/RLF procedure for robustness and latency reduction, especially for URLLC use cases
Specify features for early beam failure indication for use cases such as multi-TRP and URLLC
RP-192708

## Slide 10: Multi-Beam/Panel Enhancements
Simultaneous multi-panel transmission for IAB
    SDM: Simultaneously Tx or Rx on backhaul and access links
    Multi-Panel Tx/Rx: Simultaneously Tx/Rx on backhaul
    and access links (UEs to remain half-duplex)
    Multi-panel enhancements leads to a reduction
    in latency and more efficient frame structure for
    IAB nodes
SDM
Multi-panel Tx/Rx
SDM
Multi-Panel Tx/Rx
Improvements related to panel selection and multi-panel Tx/Rx are important for use cases such as multi-TRP, IAB, and V2X
Specify features for UL beam selection, panel selection and simultaneous transmission across multiple panels
Specify enhancements for simultaneous multi-TRP transmission with multi-panel reception
RP-192708

## Slide 11: Multi TRP Enhancements
Multi TRP transmission is a key feature for improving throughput, robustness and reliability of NR based networks particularly in FR2. Multiple use cases such as URLLC, V2X, NR-U still require enhancements in Rel. 17
Specify enhancements to URLLC based single DCI solutions for all the downlink and uplink channels
Specify enhancements to enable inter-cell multi-TRP operation
Specify enhancements to enable multi-TRP operation in FR2
CP
CP
CP
CP
CP
CP
CP
CP
Synchronous
Asynchronous
TRP 1
TRP 2
TRP 1
TRP 2
Overlapped
PRB allocation
Non-overlapped
PRB allocation
TRP 1
TRP 2
Single FFT Window
Joint Demodulation
Ideal Backhaul with joint scheduling
Joint or independent CSI
Single FFT Window
Joint Demodulation
Ideal Backhaul with independent scheduling
Joint or independent CSI
Dual FFT Window
Independent Demodulation (SIC)
Non Ideal Backhaul with semi-static resource
Partitioning
Independent CSI
Dual FFT Window
Independent Demodulation (SIC)
Non Ideal Backhaul with no coordination
(UE handles the layer partitioning)
Independent CSI
RP-192708

## Slide 12: References
[1] RP-191551, TSG RAN Chairman, “Preparing for Rel-17”, 3GPP RAN#84, Newport Beach, USA, 3-6 June 2019