## Slide 1: 3GPP TSG RAN Plenary Meeting #86 RP-192709 Sitges, Spain: December 9-12, 2019 Agenda item: 9.1.2 Source: AT&T Title: IAB Enhancements for Rel-17 Document for: Discussion/Decision

## Slide 2: IAB Enhancements - Overview
    Duplexing enhancements
    Multiplexing beyond TDM (FDM/SDM/multi-panel Tx/Rx) including multi-parent scenarios, case 6/7 timing alignment, power control/CLI optimizations
    Topology enhancements
    Mobile IAB: CP/UP split + Group mobility
    Inter-CU topology adaptation
    Mesh-connectivity between IAB nodes for local control/user plane routing
    User plane enhancements
    Multi-hop scheduling enhancement – exchange of benefit metric between IAB nodes to enable radio-aware multi-hop scheduling to improve throughput performance
    Network Coding
    Study benefits compared to duplication over redundant backhaul routes

## Slide 3: Duplexing Enhancements
Multi-panel Tx/Rx on a IAB-node (e.g. DU Tx/MT Rx) basis may have limited standards impact
Simultaneous multi-panel transmission for IAB
    SDM: Simultaneously Tx or Rx on backhaul and access links
    MPTR: Simultaneously Tx and Rx on backhaul and access links (UEs to remain half-duplex)
    Should also consider required coordination and optimizations for multi-parent scenarios
Reduction in latency and more efficient frame structure for IAB nodes
Specific Power Control/CLI characterization and mitigation enhancements for SDM/MPTR should be studied
    Ensure that access UEs are not impacted by different multiplexing alternatives
SDM
MPTR
SDM
MPTR
MPTR

## Slide 4: IAB Power Control
At the IAB node the received power level of the backhaul (DL) and access (UL) can be very different. The access (UL) is power controlled whereas the backhaul (DL) is not power controlled. Lead to significant difference is received PSD across backhaul and access.
A similar problem also happens on the transmit PSD between the backhaul and access. The backhaul (UL) and access (DL) have very different EiRP.
FDM/SDM of backhaul and access Tx/Rx functions on the same RF chains (or panels) is not possible without enhancements to power control.
The alternating frame-structure across the multiple hops leads to CLI. CLI measurement and mitigation is a key functionality to make IAB operate effectively and efficiently.

## Slide 5: Mobile IAB
  Regular (Rel-16) IAB nodes and Rel-17 mobile IAB nodes may be part of the same tree
  Separate CP and UP architecture  UP is similar to Rel-16 IAB (hierarchical tree) and CP is a single hop
    Reduces disruption and latency for downstream IAB in case of link failure/HO events
  Introduce support for “group mobility” (e.g. HO for UEs on a bus that is acting as mIAB node)
  Access UE enhancements which support awareness of IAB deployment and architecture can also be considered (e.g. based on hop count + RRM measurements)
Mobile IAB Topology
Donor
Hop 1
Hop 2
MT U-Plane
UE C/U-Plane
MT C-Plane

## Slide 6: Mesh topologies and local routing for IAB
A mesh topology for IAB is beneficial to enable more responsive inter-node coordination and to reduce user plane latency for local traffic
The mesh network could be designed to exist either independently or to co-exist with the current hierarchical IAB network design (with the existing hierarchical IAB network to exercising some control of mesh capability of IAB nodes in terms of configuration, etc.)
Multiple options are possible for the design of a new IAB-node to IAB-node interface to support mesh connectivity, however a PC5-based interface between peer IAB-MTs of two IAB nodes is preferred since it allows reuse of the existing Sidelink functionality.

## Slide 7: Multi-hop Scheduling Enhancement
    Introduce generic field at BAP layer (BAP CE or header) to allow exchange of benefit metric between child and parent IAB nodes
    Specific benefit metric need not be defined (left up to companies to innovate upon)
    Enabler for radio-aware multi-hop scheduling
    Shown to provide significant improvement to experienced user throughput:
        E.g. multi-hop scheduling metric computed based on multi-hop capacity derived from access and backhaul link effective SINR values shows significant improvement in user experienced throughput (simulation results from fully dynamic event-driven system-level simulation of an IAB network)

## Slide 8: Network Fountain Coding for IAB
Packet duplication via multiple IAB paths/links can provide good reliability but it is highly inefficient
Fountain code is an outer rate-less code applied at a higher layer (FEC at PHY is not touched)
    Fountain coded segments are transmitted over multiple paths/links
    Any combination of N coded segments from any paths can be used to decode
    Can achieve the same reliability as packet duplication with much less overhead
Fountain Encoder
Decoder
Message Passing
Path 1
Path 2
Path 3
pkt
Core
Network
IAB Donor
Access UE
Access
IAB
pkt
Any combination of 3 segments from any path is enough to decode

## Slide 9: IAB Enhancements – Proposal (1)
  Proposal: Rel-17 IAB WI should include the following objectives:
Duplexing enhancements:
IAB node resource allocation and configuration enhancements to support simultaneous multi-panel and multi-parent transmission/reception for IAB:
    SDM: Simultaneously Tx or Rx on backhaul and access links
    MPTR: Simultaneously Tx and Rx on backhaul and access links (UEs to remain half-duplex)
    Multi-parent: Mechanisms to support semi-static and dynamic resource coordination between parent IAB-DUs/donors of the same child IAB node
Support for Case 6 and Case 7 timing (as described in 38.874) to enable aligned DU/MT Rx and Tx timing
Power control enhancements to support FDM/SDM of backhaul and access Tx/Rx functions on the same RF chains (or panels).
Enhancements supporting intra-IAB node/ inter-IAB node CLI measurement and mitigation in case of SDM/MPTR
Mobile IAB:
  Separation of CP connectivity via single-hop FR1 links and UP connectivity via multi-hop FR2 link(s).
  Inter-donor topology adaptation
  Support for group mobility – optimizing and reducing impact on control plane signalling for UEs during mobile IAB node handover events
IAB-aware UE cell-selection enhancements

## Slide 10: IAB Enhancements – Proposal (2)
User Plane Enhancements
Mesh connectivity between IAB nodes for redundancy and low-latency CP/UP routing via PC5-based interface between peer IAB-MTs of two IAB nodes:
Support for CP signalling directly between IAB nodes to support resource coordination and robustness in case of backhaul link failures
Support for UP routing over mesh topologies to reduce latency for low-latency and/or local traffic
Support for both standalone mesh backhaul networks and hybrid multi-frequency mesh/hierarchical topologies
Support for backhaul scheduling enhancements at IAB nodes/donor nodes (carryover from Rel-16). Potential enhancements include transmitting a scheduling benefit metric, L1/L2 measurements, or topology information via a BAP control PDU.
Network coding
Study the following:
Protocol stack architectures applicable to fixed and mobile IAB, with and without impact to legacy UEs.
Reliability, efficiency, throughput and latency performance for small and large packet sizes compared to Release 16 packet duplication.
Network coding techniques, including rateless codes, discrete rate codes, and other potential network coding techniques with and without feedback.