## Slide 1: - Motivation – Rel-17 Positioning Integrity
Swift Navigation, Deutsche Telekom
RP-192750
3GPP TSG RAN#86
Sitges, Spain
December 9th -12th 2019
Agenda Item: 9.1.2

## Slide 2: Positioning Integrity: Motivation
Rel-16 defines high accuracy GNSS extensions at < 10cm using State Space Representation (SSR).
TS 22.261 requires trustworthiness in the positioning data and system:
  The 5G system shall be able to determine the reliability, and the uncertainty or confidence level, of the position-related data.
TR 22.872 defines trustworthiness as Positioning Integrity:
  A measure of the trust in the accuracy of the position-related data provided by the positioning system and the ability to provide timely and valid warnings to the UE and/or the user when the positioning system does not fulfil the condition for intended operation.
Positioning Integrity was identified as an area of Study following initial SSR support:
  RP-1804428 Report of email discussion [99bis#57][LTE/Positioning] Future phase support of SSR
  TR 22.872 Study on positioning use cases
  RP-191919 Views on Release 17 Positioning Enhancements
Rel-16 did not define assistance data to verify Positioning Integrity.
RP-191919 reviews Positioning Integrity considerations for 3GPP Rel-17.
¹ Note: For the purpose of this discussion “Positioning Integrity” refers to the trustworthiness of the GNSS navigation outputs and not the alternative 3GPP meaning of ensuring that a message is transmitted without errors over a communications channel. These concepts and distinctions can be further refined in the Study Item.

## Slide 3: Positioning Integrity: Background
Positioning Integrity conveys to the user the reliability of the information received & computed.
Timely warnings are provided when data should not be used.
Positioning Integrity is currently used for commercial aviation, which does not address high accuracy.
High accuracy (< 1m or better) means certain errors are no longer absorbed within the nominal error budget (e.g. 10s or 100s of meters).
The effects of additional errors must therefore be determined at the required confidence level e.g.
  Multipath effects in different application environments (e.g. open sky vs. urban areas)
  Atmospheric effects such as high frequency ionospheric or tropospheric changes
  Satellite or control system failures
  Local UE bias effects such as GNSS phase cycle slips
These errors can be modelled (e.g. using SSR) and detected with an associated confidence level.
Confidence information must be available to the UE in order to compute it’s Positioning Integrity.
High accuracy requires monitoring and signaling of Network-side and UE-side Integrity KPIs.
These concepts are illustrated in Appendix A.

## Slide 4: Positioning Integrity: Use Cases
Positioning Integrity can be applied to any positioning use case.
It is crucial to Mission Critical and Safety Critical applications.
Road users are a priority use case driven by Service Providers, OEMs, Component Suppliers & Regulators, including:
  V2X and autonomous vehicles
  Emergency calls and first responders
  Vulnerable road users
  Road-user charging and lane-level services
  Asset tracking and mobility management
  High definition mapping
Positioning reliability / integrity are being defined in road user requirements, e.g:
  TR 22.872 - Study on positioning use cases (3GPP, 2018).
  GNSS Market Report, Issue 6 (GSA, 2019).
  C-V2X Use Cases Methodology, Examples and Service Level Requirements (5GAA, 2019).
  Analysis of GNSS correction data standards for the automotive market (Vana et al., 2019).
  GNSS Correction Services (u-blox, 2019).
There is no industry standard for Positioning Integrity today.
Positioning Integrity is critical to delivering 3GPP positioning use cases.

## Slide 5: Rel-17 Work Item on Positioning Integrity
Positioning Integrity is a requirement for high accuracy applications supported by the 5G system.
LTE Positioning Protocol does not yet include information elements to validate Positioning Integrity.
Positioning Integrity requires Network and UE-side assistance information.
The applications requiring Positioning Integrity will be limited to User Plane if Positioning Integrity is not supported at Control Plane through LPP. This will significantly limit the adoption of positioning via 3GPP.
Rel-17 is a logical and necessary extension to the positioning support enabled by Rel-16.
Proposed Work Item for Rel-17:
  Identify Positioning Integrity KPIs for relevant use cases.
  Identify & study the error sources, threat models, occurrence rates and failure modes requiring Positioning Integrity validation and reporting.
  Examine existing methodologies and gaps for network-assisted and UE-assisted integrity.
  Based on the outcome of the study in 1, 2 & 3, specify an approach to network-assisted Positioning Integrity in support of high accuracy positioning by extensions to LPP and related network and UE protocols.

## Slide 6: Appendix A: Primer on Positioning Integrity
The primary output is the user’s Estimated Position.
  This estimate will contain some error compared to the True Position.
To indicate the quality of the position, the Accuracy is also estimated. This is typically given as e.g. a 1 sigma (68%) value.
  This indicates 68% of position outputs are better than the reported accuracy.
  This leaves 32% of positions worse than the stated accuracy - but how much worse?
For high accuracy positioning, we want to bound the error to a much higher level of confidence. This is the concept of Positioning Integrity
  Alert Limit (AL) is an upper bound on position error.
  Alert Limit is calculated for a Target Integrity Risk (TIR).
  TIR gives an allowable rate of occurrence of error greater than the Alert Limit e.g. less than once per 100,000 hours (< 10-5/hour).
Estimated
Position
❌
True
Position
Accuracy
❌
Alert Limit
❌

## Slide 7: Appendix A: Primer on Positioning Integrity
To compute the Alert Limit for a low TIR it is not sufficient to consider nominal performance only.
Rare fault conditions and “feared events” must be considered
  e.g. degradation / failure of the GNSS satellite.
These faults can be difficult to detect on the UE alone.
To achieve necessary integrity KPIs, it’s essential for the GNSS network to monitor for certain faults and provide assistance data to the UE to support integrity computation.
Network-side faults must be monitored and communicated,
e.g. satellite feared events, atmospheric events, network events
Service
User Equipment
Example Fault Tree