## Slide 1: Motivation for new SI proposal on sidelink-based relay in NR
OPPO
3GPP TSG RAN Meeting #86 RP-192751
Sitges, Spain, December 9 – 12, 2019
Agenda item: 9.1.2
Document for: Discussion
Notes: 多谢

## Slide 2: Use of high frequency spectrum
From network perspective
  Higher frequency band should be explored for NR
  Challenging to provide full network coverage at high frequency spectrum
  Beneficial to improve spectrum utilization of the precious frequency resource, in a way other than simply deploying denser network infrastructure
From UE perspective
  It is also costly to be equipped with module(s) supporting high frequency band
  Necessary to further explore further uses of the high-frequency band module for more services, and not limited by the hot-spot coverage
=> The usage of sidelink would be one tool to extend coverage for both Uu and PC5 interface

## Slide 3: Background of sidelink and applications
Sidelink development in 3GPP
  In Rel-12/13, ProSe was introduced and mainly optimized for voice type traffic (MCPTT), i.e., lower data rate, relaxed delay requirement
  In Rel-14/15/16, V2X was introduced for ITS operation and power efficiency is not fully taken into account, i.e., energy-efficiency is traded off for coverage and safety
In NR-V2X, so far only vehicle-based terminal and services have been considered
  SA1 studying on more use cases for commercial sidelink services, i.e. SID of “Network Controlled Interactive Service” (TR 22.842)
  With the expectation that 5G portable UEs, existing or some new form devices (e.g. VR/AR devices, robot, etc.) are to be used for local services, e.g. entertainment in home / party / bar / gaming venues, or education in office
  These requirements need to be reflected by further work in both RAN and SA

## Slide 4: Operating scenarios for sidelink-based relay
4
Uu Coverage
Uu Coverage Extension
Uu
PC5
SL Coverage Extension
SL Coverage Extension
In-coverage relaying
Partial/Out-of-coverage relaying

## Slide 5: Existing work in SA: NCIS in SA1
Key aspects having been finished
  KPI Table related to interactive services, e.g. VR/AR based gaming
  All ProSe related requirements have been clarified
  Group related requirements have been clarified
Completion level and next step
  Reported 100% in SA#86 (Dec 2019)
  Technical Report available in TR 22.842

## Slide 6: Existing work in SA: 5G_ProSe in SA2
To develop a common framework for supporting proximity based services (to satisfy service requirements defined for both public safety and commercial proximity services)
Set A: System enhancements to support Public Safety related proximity services:
Based on the common framework, this part focuses on system enhancements to support service requirements defined for public safety services
Set B: System enhancements to support commercial related proximity services:
Based on the common framework, this part focuses on the commercial specific proximity services
Completion level and next step
  Reported 40% in SA#86 (December 2019)
  Completion by June/2019
  Technical Report available in TR 23.752

## Slide 7: SL-Relay email discussion output
  Based on the email discussion result
  The following aspects are supported by clear majority view
  Include a RAN2-led sidelink relaying item into the Rel-17 package (All),
  Start Rel-17 sidelink relaying as a SI with a follow-up WI in Rel-17 (16/31, while 9/31 are fine with either or tend to see that as scope-dependent).
  At least single-hop UE-to-network relay (31/33) and single-hop UE-to-UE relay (28/33). Pending RAN#86 decision on the need of multi-hop.
  Rel-17 sidelink relaying item includes at least objectives on
    1) Relay (re-)selection criterion and procedure (32/33),
    2) Relay/Remote UE authorization (32/33),
    3) QoS for relaying functionality (30/33),
    4) discovery model/procedure for relaying functionality (29/34).

## Slide 8: SL-Relay email discussion output
  Based on the email discussion result
  The following technical aspects are to be further discussed, i.e., whether to include into as objectives
  Cross-RAT Uu configuration of sidelink relaying,
  service continuity during path switching between direct Uu connection and PC5 relayed connection;
  inter-PLMN discovery operation;
  UE cooperation functionality;

## Slide 9: SL-Relay email discussion output:
For the down-selection to be made w.r.t. L2/L3, which is the main issue according to the email discussion
15/31 companies express preference on L2 relay;
4/31 companies express preference on L3 relay;
12/31 companies did not provide a clear preference;.
  There are two possible options as follows – to be concluded in RAN#86
  Option 1: L3 relay in Rel-17, covering both UE-to-network and UE-to-UE relay (e.g., ~1.5TU per RAN2 meeting, with 2 quarters for SI, converted into WI afterwards)
  Option 2: L2 relay in Rel-17, covering UE-to-Network, with UE-to-UE relay being down-prioritized, and clarify the assumption of relaying architecture, i.e., end-to-end PDCP and hop-by-hop RLC as concluded in FeD2D/IAB, to avoid further discussion on architecture alternative. (e.g., ~2TU per RAN2 meeting, with 3 quarters for SI, converted into WI afterwards)
  => RAN#86 to down-select between option-1 and option-2