## Slide 1: Overview on RAN Proposals for Rel-17
3GPP TSG-RAN Meetings #86 RP-192755
Sitges, Spain, 9th Sep.– 12th Sep. 2019
Agenda item: 9.1.0

## Slide 2: General view
1, 15 months for Rel-17 is fine, but 18 months could provide more flexibility
2, Dedicated TUs should be reserved to stabilize Rel-16 specifications. LTE and NR TUs should be in the same pool for Rel17. Make sure there is no hidden TUs in case of parallel sessions except for TUs for flexible meeting arrangement by taking offline discussion into account. Reasonable close of session is pretty much welcome 
3, Package approval: Rel-17 Package is approved in RAN#86 and slow start from Q1/Q2 2020 for RAN1 and RAN2/3/4 respectively

## Slide 3: RAN1 leading WID/SID
WID/SID | Brief description
General Sidelink | Leftover: SL CSI,Mode-2d,PC for GC,PFSCH New: SL MIMO/BF,CA,FR2,DRX
MIMO | FDD partial reciprocity, CSI for high speed UE, multi-TRP transmission, UL throughput and coverage, multi-beam operation.
URLLC/IIOT | HARQ-ACK retran/mux, out of order scheduling, UE/packet based duplication, Intra-UE MUX,UE specific cancellation, SPS/CG resource efficiency, EHC and TSC enhancement
UE Power Saving | CDRX for FR1/FR2, dynamic PDCCH skipping w/o DRX e.g. for AR/VR, faster BWP switch with more side functionality e.g. CSI, Paging reliability and RRM relax in IDLE/INACTIVE
NR Light | IWSN, wearable device and surveillance camera. Lower UE capacity (Antenna, UE BW,HD FDD), Power saving for IDLE/INACTIVE with long DRX, Coverage compensation for DL
Coverage | FR1: Outdoor2indoor, rural area; VoIP and low rate eMBB, focusing uplink FR2: indoor and dense urban; service and channel to be evaluate
XR | Cloud gaming and AR/VR; traffic model and performance evaluation
Others | Open to include Positioning and >52.6GHz with reasonable scope

## Slide 4: RAN2/RAN3 leading WID/SID
WID/SID | Brief description
Sidelink Relay | UE to network relay, UE-UE relay, L2 or L3
Small data | INACTIVE state only; UL&DL; 2/4-step RACH
Multi-SIM | Up to 2 SIM, both intra/inter-PLMN, focus on collision between paging/state transition and data transmit or simultaneous/TDM data transmission, focus on SA LTE and SA NR
UDC | Replant LTE solution for UL only
Slicing | Fast access to intended slice and service continuity during HO
RAN data collection | Some Rel-16 leftover e.g. Network power saving, load balancing, and mismatch issue between network and UE
Multicast broadcast | V2X, Public safety, Video/audio efficiency improvement, NR SA only within limited area, FR1 first , no additional signal/channel/numerology
Others | Open to include NTN, IAB but with reasonable scope. E.g. NTN only cover normative work on LEO and GEO, but no positioning and IOT. IAB to cover e.g. new duplex mode but no mesh connectivity and NR-U etc.

## Slide 5: Closing of R16 V2X and impact on R17 SL items
As already announced by RAN1 chairman, RAN1 work on Rel-16 5G-V2X is completed, remaining details to finalized by maintenance CRs
  No impact to Rel-17 package approval in RAN#86 and starting time for R17 sidelink related items
  In RAN#86 (Dec’19), R16 5G-V2X WID should be updated to remove some incomplete features/functionalities
    Simultaneous configuration of mode 1 and mode 2 for a UE
    MIMO: 2-layer transmission and RI feedback
    Slot aggregation
    Resource pre-emption
Regardless of remaining R16 5G-V2X work is to be handled via maintenance CRs or a dedicated AI/TU in RAN1, the following principles should be followed to ensure normal closure of this WI in RAN#87 (no exception sheet) and avoid any impact to the work on R17 sidelink items
  Handling of remaining work in 2020-Q1/2 should have no / minimize impact to RAN2 (preferably no new RRC parameters / UE features)
  Strive to finish basic functionalities according to WID objectives
  No new features, enhancements or optimizations to the basic functionalities
  Previously endorsed RAN guidance of reusing existing NR Uu and LTE V2X design as much as possible

## Slide 6: R17 General Sidelink Enhancements (OPPO preferred topics)
  Left-overs from R16
    SL CSI: PMI, CSI for GC, CSI to network
    Mode-2d
    SL PC for GC
    PSFCH: Long format, CBG based FB, PC
  New functions for R17
    SL BF/MIMO enhancement
    Multi-carrier operation, FR2
    Power saving
    DRX (RAN2)

## Slide 7: R17 SL-Relay email discussion output
  Proposal 1 Include a RAN2-led sidelink relaying item into the Rel-17 package, covering both single-hop UE-to-network relay (29/31) and single-hop UE-to-UE relay (27/31). Pending RAN#86 decision on the need of multi-hop.
  Proposal 2 Rel-17 sidelink relaying item includes at least objectives on 1) Relay (re-)selection criterion and procedure (31/32), 2) Relay/Remote UE authorization (31/32), 3) QoS for relaying functionality (29/32), and one objective on 4) discovery model/procedure for relaying functionality (27/32).
Proposal 3 RAN further discuss the need of objectives on: 1) Cross-RAT Uu configuration of sidelink relaying, 2) service continuity during path switching between direct Uu connection and PC5 relayed connection; 3) inter-PLMN discovery operation; and 4) UE cooperation functionality;

## Slide 8: R17 SL-Relay email discussion output:
For the down-selection to be made w.r.t. L2/L3,
13/29 companies express preference on L2 relay;
4/29 companies express preference on L3 relay;
12/29 companies did not provide a clear preference;.
  There are two possible options as follows – to conclude in RAN#86
  Option 1: L3 relay in Rel-17 and leaving L2 potentially for future release
  Option 2: L2 relay in Rel-17
  Proposal 4 Decision on L2/L3 will be made at RAN#86.
  Proposal 5 Start Rel-17 sidelink relaying as a SI with a follow-up WI in Rel-17 (14/29, while 9/29 are fine with either or tend to see that as scope-dependent).