## Slide 1: Key points on Rel-17 enhancements for NB-IoT
Huawei, HiSilicon
3GPP TSG RAN Meeting #86
Sitges, Spain, December 9-12, 2019
RP-192793

## Slide 2
Justification
As the enabler of various LPWA use cases for massive IoT (e.g. sensors, metering, smoke detector, etc.), cellular IoT technologies NB-IoT and LTE-MTC have been successfully commercialized over the world. Issues observed from real deployment and foreseen market demands should have high priority to be addressed in the Rel-17 evolution.
One of the design purposes for NB-IoT is to allow re-farming 200 kHz GSM carriers. NB-IoT module cost is already comparable to GPRS. The evolution needs to not only provide outstanding LPWA experience but also ensure the eco-system is able to carry existing 2G M2M service which mainly happen in normal coverage (CE0).
We have observed market demands to require higher data rate for NB-IoT. It can extend the application use cases in already-deployed networks and also benefit for power saving e.g. by reducing time for FOTA firmware update.
We also highlight an issue from real deployment for existing RLF-based cell change.

## Slide 3: Issue from real deployment for NB-IoT RLF enhancement
Observation
  In existing 2G networks >50% of M2M service is in mobile cases (e.g. vehicle tracking in 29%).
  We test NB-IoT vehicle tracking equipment in real networks, and radio transmission failure is more frequent than with GPRS, since (RLF based) cell change latency is much higher.
Traffic model | Scenario
Content: vehicle status, location update, etc. Frequent report every 5-10s | Vehicle mobility Not power consumption sensitive
Vehicle tracking
NB-IoT now only supports radio link failure (RLF) and re-establishment for connected mode mobility: this results in very late cell change in this case.
Suggestion
  Urgent demand to improve mobile M2M service in NB-IoT
    Enlarge market besides LPWA
    Speed up replacing 2G network
    Ensure service experience migrating from GPRS is maintained
  Rel-17 WI objective: Improvement of RLF based cell change
    Enhancements to measurement trigger and RLF procedure
Measurement trigger
before RLF
Finish re-establishment more quickly
2G/NB-IoT
LPWA/NB-IoT
Vehicle tracking
POS equipment
144dB
Metering
Smoke alarm
164dB
20dB coverage

## Slide 4: Market demands for higher data rate NB-IoT
  Observations:
      We see market demands to extend use case and support more applications e.g. related to human experience which requires higher data rate e.g. health/fitness, Smart POS.
      Higher data rate also benefit to save time for FOTA firmware update and hence save UE power consumption.
      There are deployment scenarios where there is not enough BW (1.4 MHz) to deploy LTE-MTC.
    Solutions:
      Introduction of 16-QAM can increase peak data rate only for good coverage UEs. 16-QAM requires higher demodulation SNR than QPSK.
      Supporting wider bandwidth transmission, e.g. CA, using multiple NB-IoT carriers can increase data rate for all UEs. (Maintaining same SNR as single carrier)
Proposals:
      Include 16-QAM for unicast UL and DL in Rel-17 NB-IoT work
      Include wider-bandwidth NB-IoT transmission in up to 3 NB-IoT carriers in Rel-17 NB-IoT work

## Slide 5
We highlight two other aspects we think are worthwhile to have in Rel-17 LTE IoT work, even though there is not a majority interest in the email discussion:
Frequency hopping between NB-IoT carriers.
Inter-RAT operation between NB-IoT/LTE-MTC and NR.
Other aspects

## Slide 6: Frequency hopping in NB-IoT
  NB-IoT supports multiple carriers, via anchor and non-anchor carriers, from Rel-13
  When several carriers are already deployed at system level, it makes sense to exploit frequency hopping gain between carriers to save scheduling resource and UE power consumption
  It has no UE complexity impact
    Frequency hopping interval: 1PRB (~1.8dB gain)
Proposal:
      Include frequency hopping among NB-IoT carriers in Rel-17 NB-IoT work
    Frequency hopping interval: 4 PRB (~3.5dB gain)

## Slide 7: Inter-RAT operation for LTE LPWA IoT
    Inter-RAT operation:
      It is natural to support inter-RAT mobility between NB-IoT/LTE-M and NR in Rel-17. NB-IoT already supports cell selection assistance for LTE/LTE-M/GSM in Rel-16 and this should be extended to cover NR cell selection for multi-mode terminals.
      Rel-15/16/17 NR do not address LPWA. Inter-RAT operation between LPWA and non-LPWA for a multi-mode UE can allow support for various use cases within a single device. A multi-mode UE with NB-IoT/NR or LTE-MTC/NR would not have too much difference in comparison with NB-IoT/LTE multi-mode UE (idle mode cell selection assistance supported in Rel-16) in terms of device cost, especially consider NR-Light.
Proposal:
      Include inter-RAT cell selection for NB-IoT/LTE-MTC to and from NR in Rel-17 work
NB-IoT/LTE-M
NR
LPWA
Non-LPWA
better coverage
power saving in idle mode