## Slide 1: Views on Sidelink Enhancements in Rel-17
China Academy of Telecommunications Technology (CATT)
3GPP TSG RAN Meeting #86 RP-192857
Sitges, Spain, December 9th -12th , 2019

## Slide 2: Vision of 5G
5G is expected to change every aspects of modern society
  Smart city, education, health, industry, transportation, environment, entertainment, finance, agricultures…
Agriculture
Health
Education
Transportation
Finance
Environment
Wearable devices
Home
AR
VR
Entertainment
Cloud
Mobile device
Industry

## Slide 3: V2X Evolution in Rel-17
Better user experience
  Personalized services – toward auto-driving car and automobile safety
  Optimizing user perceived throughput through both Uu link and sidelink
  Minimizing mobile phone power consumptions
    UE power consumption reduction in V2P
Traffic control
  V2X communication in assisting the optimization of traffic control
Safety
  Enhance the safety of auto-driving through V2X communication
    Pedestrian sensing and V2P communication
  Network broadcast/multi-cast in support of safety related information broadcast to vehicles

## Slide 4: Motivation of Rel-17 NR V2X
Target use case of Rel-17 NR V2X, advanced V2X service, including vehicles platooning, extended sensors, advanced driving and remote driving.
Specify all the aspects studied in Rel-16 NR V2X SI but not included in Rel-17 V2X WI
  Features specific to FR2 could be addressed in Rel-17
  Rel-17 NR V2X focuses on the design aspects of NR sidelink, some Uu enhancements would be left for future release, e.g., broadcast/multicast.
    V2X broadcast and group cast are the main use cases of Uu broadcast/multicast
Rel-17 NR V2X addresses the coverage issues
  Range extension of Uu control V2X applications and sidelink V2X applications

## Slide 5: Rel-17 D2D Direct Communication and Discovery
User-oriented system evolution –
  Better user experience is one important aspects in marketing NR and further development
  Enhancement of Sidelink for D2D
    Direct communication –
      Achieve high data rate and low latency
      Increase the radio resource reuse through sidelink
    Discovery –
      Support of applications of proximity services (e.g., social media, peer discovery)
      Assistance in coverage extension of direct communication
Extended 5G vertical domain through sidelink enhancement for D2D
  D2D communications between different devices types
  Extended user applications through D2D direct communication

## Slide 6: Requirements for D2D
Spec | Requirements
TS22.278 | D2D discovery for both commercial and PS services should be supported; D2D communication should be supported at least for PS services.
TS22.261 | UE-to-network relay should be supported: Connection between remote UE and relay UE can be 3GPP RAT or non-3GPP RAT； UE using simultaneous indirect and direct network connection should be supported; Connection between remote UE and relay UE can be licensed or unlicensed band; 5G system with satellite access should be considered.
TS22.125 | D2D broadcast communication should be supported for UAV: Support direct UAV to UAV local broadcast communication at relative speeds of up to 320kmph with variable message payloads of 50-1500 bytes.

## Slide 7: Sidelink Enhancement for D2D
NR proximity service requirements | Sidelink Enhancement for D2D
Sidelink discovery | The sidelink discovery requirements in V2X is limited to application triggered peer discovery for unicast and groupcast For commercial cases (e.g. advertisements) or public safety cases (e.g., disaster alarm), the discovery message needs to be transmitted frequently. Efficient resource utilization is essential.
UE-to-network and UE-to-UE relay | UE-to-network and UE-to-UE relay are essential in extending the range of the communication. There is clear requirement of relay from SA2.
Sidelink communication | D2D has different deployment scenarios and requirements compared with those of V2X. The D2D deployment scenarios are mostly indoor with low mobility and high penetration loss. The power consumption needs to be low for D2D comparing to that of V2X. The sidelink link adaptation and interference management for D2D are different to those of V2X.

## Slide 8: Motivation of NR sidelink for D2D
SA2 requirements of sidelink enhancement for D2D
  TS22.278 defined requirements on discovery for both commercial and PS
    Discovery procedure and related messages are up to upper layers in NR V2X
  TS22.261 defines requirement on support of UE-to-Network relay
    UE relaying resource (pool) configuration is not supported in Rel-16 V2X work
Sidelink Enhancement
  Evaluation of deployment scenarios of D2D for public safety and commercial services
    Indoor scenarios with large penetration loss
    Outdoor scenarios with extended coverage
  Sidelink enhancement in support of D2D communication –
    Coverage extension – PSSCH beamforming
    Higher data rate - multi-antenna operation and carrier aggregation
  D2D proximity discovery
    D2D discovery in support of applications (e.g., social media)
    D2D discovery to assist direct communication – network-to-UE and UE-to-UE relay
    Multi-carrier discovery – NR and LTE discovery
  Device power saving

## Slide 9: High Level Requirements for Rel-17 Sidelink Enhancement
Increased data rate - Sidelink multi-carrier operation can be considered.
Enhanced reliability and reduced latency
  Enhancement of mode 2 resource selection
  Effective congestion control
Support of new carrier frequencies and operation scenarios
Power saving
  Sidelink DRX operation
  Enhancement of sensing and resource selection
Spectral efficiency enhancement
  Enhancement of multi-antenna techniques
Sidelink coverage enhancement – UE-to-UE relay
Network coverage enhancement – UE-to-network relay

## Slide 10: Rel-17 Sidelink Enhancement
Evaluation of deployment scenarios of D2D for critical communication and commercial services
  Indoor scenarios with large penetration loss
  Outdoor scenarios with extended coverage
Extend the SL framework to support D2D services for PS and commercial use cases
  Optimization of NR resource utilization through direct communication
Sidelink multi-carrier operations for V2X and D2D
  Aggregation of SL communication in ITS and commercial carriers
UE-to-NW and UE-to-UE relay operation, including
  Relay UE discovery and selection procedure
  Relay UE coordinated transmission mechanism to improve link reliability
  Sidelink beamforming and beam management for FR1 and FR2
Sidelink enhancement for V2P and D2D
  Enhancement of resource allocation and sensing/collision avoidance mechanism for Pedestrian-UE
Enhancement on multiple antenna techniques
Study D2D proximity discovery
  Study NR sidelink physical layer structures, procedure(s), and L2/L3 protocols for D2D proximity discovery in single and multi-carrier
  Study the interaction between NR D2D discovery and LTE D2D discovery
  Study the D2D proximity discovery in assistance of UE-to-network relay and UE-to-UE relay
Study the device power saving techniques for V2P, D2D discovery and D2D directly communication