## Slide 1: Motivation for WI on 1024 QAM
3GPP TSG RAN meeting #86 RP-192928
Sitges, Spain, Dec 9-12, 2019

## Slide 2: Background
LTE supports 1024 QAM since Rel-15.
  The feasibility and benefits for this modulation scheme are captured in TR 36.783.
Due to this, the peak spectral efficiency of NR is lower than that of LTE (for the same number of layers).
1024QAM provides throughput gains in high geometry scenarios (e.g. indoor, CPE), as shown in the outcome of the study phase for LTE (some examples in next slide)

## Slide 3: Benefits of 1024QAM
Gains observed in high SNR scenarios:
  For 2T2R under TDL-D/E channel with correlated LOS, 1024QAM provides performance gain of 0-11% at 30dB SNR for TX EVM less than or equal to 2%.
  For 2T4R under TDL-D/E channel with correlated LOS, 1024QAM provides performance gains of 11-16% at 30dB SNR for TX EVM less than or equal to 2%.
  For 2T2R under TDL-D/E channel with uncorrelated LOS, 1024QAM provides performance gain of 0-19% at 30dB SNR for Tx EVM less than or equal to 2%.
  For 2T4R under TDL-D/E channel with uncorrelated LOS, 1024QAM provides performance gain of 8-22% at 30dB SNR for Tx EVM less than or equal to 2%.
  For 2T2R and 2T4R TDL-D/E channel with uncorrelated LOS, 1024QAM provides performance gains of 16-22% gain at 35dB SNR.
Some statements from TR 36.783

## Slide 4: Scope of work
For LTE Rel-15, the work for 1024QAM used many time units due to the study phase
  Benefits needed to be shown before moving to normative phase.
Given the similarity between NR FR1 and LTE, the LTE work can be heavily leveraged:
  Reuse gNB EVM requirements from LTE
  Reuse constellation definition from LTE
With this, the work for 1024QAM can be completed in Rel-17 with a reduced number of time units.
Leverage the work in LTE

## Slide 5: An estimate of RAN1 TUs
The normative phase for 1024 QAM comprised 3 TUs in the following meetings:
NR should be able to complete the work in less than 3 time units:
  For LTE, the 3 TUs also included work for DMRS overhead reduction (shared WI)
  For LTE, the TBS determination method required to exhaustively fill the TBS table (several hundred entries) + mapping to multiple layers. For NR, this procedure is greatly simplified.
  For LTE, there was a discussion on the modulation mapping, which should be avoided in NR.
Estimate: 2 TUs in RAN1 should be enough to complete the work.
Comparison with LTE
Meeting | Agreements
RAN1#90b | Agreed on modulation mapping, capabilities, configuration
RAN1#91 | Principles for TBS determination, email discussion to decide CQI/TBS entries
RAN#92 | Final details + mapping of TBS to multiple layers

## Slide 6: Proposal
For Rel-17, approve a RAN4-led work item to specify 1024QAM for PDSCH in FR1 with the following objectives:
  RAN4:
    Base station requirements (EVM requirements reused from LTE)
    UE demodulation requirements
  RAN1:
    Introduce 1024QAM modulation (copied from LTE)
    Define new CQI table.
    Define new MCS index table.
  RAN2:
    Define corresponding capabilities and configuration parameters.