## Slide 1: Proposed Way Forward on RRM Requirements for the IAB Project
Qualcomm Inc, AT&T, KDDI
3GPP TSG-RAN Meeting #86 Sitges, Spain, December 9th – 12th , 2019
RP-192949

## Slide 2: Background (I)
RAN4 has discussed the definition of RRM requirements for IAB nodes for several meetings, however, very few agreements have been reached
Currently agreed list of requirements to be introduced(see Annex) has very few requirements and is missing some key requirements that would ensure fallback even when the link fails
Several WFs to introduce requirements were presented [1] ,[2], however, few companies are objecting with the sole argument that since Rel.16 IAB deployments are planned, there is no need for any requirements as RRM event(e.g. link failure, beam switch, etc) will happen extremely seldom(if ever)
RAN1/2 have spent a considerable amount of time on defining procedures for topology change/adaptation, basic RAN4 requirements are needed to ensure good interoperability between nodes

## Slide 3: Background (II)
At least requirements for Radio Link Monitoring(RLM) and beam recovery(BFD/BFR) based on SSB and CSI-RS are needed for the MT to ensure there is a fallback mechanism if links fail
  Additional complexity incurred by the node due to these procedures is minimal since MT has to perform frequency and time tracking of the DU-MT link
  Requirements could be simplified relative to the requirements defined for UE(e.g. assume only a single RS is configured as RLM-RS, extend the monitoring period, etc)
  Without RLM it is also difficult to test RRC re-establishment since this is normally triggered by RLF

## Slide 4: Way Forward
RAN4 will introduce RLM and BFD/BFR requirements for the MT

## Slide 5: References
[1] R4-1915798, “Qualcomm Inc., AT&T, Nokia, CMCC”
[2] R4-1912715, “Qualcomm Inc., Samsung, AT&T, Docomo, KDDI

## Slide 6: Annex

## Slide 7: List of agreed requirements (I)
Requirements | Comments | Is requirement needed?
Cell reselection | Intra-frequency Inter-frequency | No
Handover |  | FFS
RRC Connection Mobility Control | RRC re-establishment Random access RRC release with redirection | Yes
SCell activation/deactivation delays |  | No
Interruptions related to SCells addition, release, activation, deactivation | Interruptions on serving cells due to any of the addition, release, activation, or deactivation procedures | No
PSCell addition/release delays |  | No
Active BWP switching | Interruptions at active BWP switching Active BWP switching delay | No
TCI switching | TCI switching delay | FFS

## Slide 8: List of agreed requirements (II)
Requirements | Comments | Is requirement needed?
RLM | Requirements for RLM, e.g., based on SSB, CSI-RS or both | FFS
Link recovery procedures | Requirements for SSB-based and CSI-RS based BFD and CBD | FFS
Measurements requirements (time duration, number of cells, etc.) |  | FFS
Measurement accuracy requirements |  | FFS
MT timing related requirements | MT transmit timing (Te and Tq) Timing Advance | Yes
 | MRTD MTTD | Yes pending introduction of CA combinations
Switching time between MT and DU | --- | TBD in RAN4 RF session
DU timing related requirements | 3 us requirement | Yes
 |  | FFS
 | T_delta command |