## Slide 1: Discussion on the scope of NR Multicast/Broadcast in Rel-17 CHTTL
3GPP TSG-RAN Meeting #86 RP-192969 Sitges, Spain, December 9-12, 2019

## Slide 2: Backgrounds
After Phase 1 email discussion for NR Rel.17 multicast/broadcast, moderator proposed to focus only on NR Standalone architecture (i.e. gNB connected to 5GC only)
  Moderator summery in RAN#85[1]
  There are at least 9 inputs mentioned NR multicast for NSA, also NR SA is not mentioned by everyone (not by us).
We still think there is a need to consider NR multicast/broadcast on NSA, especially for EN-DC architectures.
Moderator Summary | We received 27 inputs from 31 companies. Beside NR SA, mentioned by everybody, only 9 inputs mentioned NSA, some with lower priority. No other architecture options was mentioned.
Moderator Proposal | Focus only on NR SA, also because solutions for NSA already exist.

## Slide 3: Wayforward on Rel.17 multicast/broadcast
Reasons for Rel.17 multicast/broadcast support under EN-DC architectures, EN-DC with multicast/broadcast on NR SCG .
  Initial deployments are based on EN-DC.
  Compared with LTE, NR has larger bandwidth, larger capacity which make NR more suitable for some localized high data rate multicast services.
  Currently LTE cells are experiencing high load in some traffic hotspot areas, enable multicast/broadcast on NR SCG can provide less capacity impact on those LTE cells and legacy LTE traffics.
Based on above, we think it is beneficial to consider multicast broadcast support for EN-DC NR SCG.
Proposal:
  Not to preclude EN-DC architecture from the scope of Rel.17 NR multicast broadcast WI.

## Slide 4: Reference
[1] RP-191859 Summary of moderated email discussion on Rel-17 NR multicast broadcast Huawei Telecommunication India, RAN#85
[2] RP-191899 Views on NR Multicast/Broadcast in Rel-17 vivo, RAN#85