## Slide 1: Proposed Way Forward on RRM Requirements for the IAB Project
Qualcomm Inc, AT&T, KDDI, Samsung, Telstra, Ericsson
3GPP TSG-RAN Meeting #86 Sitges, Spain, December 9th – 12th , 2019
RP-193199

## Slide 2: Background (I)
RAN4 has discussed the definition of RRM requirements for IAB nodes for several meetings, however, very few agreements have been reached
Currently agreed list of requirements to be introduced(see Annex) has very few requirements and is missing some key requirements that would ensure fallback even when the link fails
At least RLM and BFD/BFR requirements would be needed in some scenarios to ensure there is a fallback mechanism in case of beam/link failure

## Slide 3: Way Forward
RAN4 will introduce RLM and BFD/BFR requirements for the MT targeting certain scenarios classes depending on RAN4 definition
  Requirements will be defined for scenarios not targeting macro type of deployments. No requirements will be defined for scenarios targeting macro type of deployments:
    If multiple MT classes (e.g. macro type, pico type deployments) are defined, the requirements should be defined only for the MT classes not targeting macro type of deployment.
    If a single MT class is defined, the requirements should be defined for the DU class not targeting DU macro type of deployment.
  Rel.15 UE requirement framework for RLM and BFD/BFR will be taken as baseline

## Slide 4: Annex

## Slide 5: List of agreed requirements (I)
Requirements | Comments | Is requirement needed?
Cell reselection | Intra-frequency Inter-frequency | No
Handover |  | FFS
RRC Connection Mobility Control | RRC re-establishment Random access RRC release with redirection | Yes
SCell activation/deactivation delays |  | No
Interruptions related to SCells addition, release, activation, deactivation | Interruptions on serving cells due to any of the addition, release, activation, or deactivation procedures | No
PSCell addition/release delays |  | No
Active BWP switching | Interruptions at active BWP switching Active BWP switching delay | No
TCI switching | TCI switching delay | FFS

## Slide 6: List of agreed requirements (II)
Requirements | Comments | Is requirement needed?
RLM | Requirements for RLM, e.g., based on SSB, CSI-RS or both | FFS
Link recovery procedures | Requirements for SSB-based and CSI-RS based BFD and CBD | FFS
Measurements requirements (time duration, number of cells, etc.) |  | FFS
Measurement accuracy requirements |  | FFS
MT timing related requirements | MT transmit timing (Te and Tq) Timing Advance | Yes
 | MRTD MTTD | Yes pending introduction of CA combinations
Switching time between MT and DU | --- | TBD in RAN4 RF session
DU timing related requirements | 3 us requirement | Yes
 |  | FFS
 | T_delta command |