## Slide 1: On mandatory features without capability signalling and number of antenna ports
ORANGE, [Telecom Italia, BT, Deutsche Telekom, Telia Company, Vodafone, Nokia,...]
3GPP TSG RAN#87e 16 – 19 March 2020 E-meeting | TDoc RP-200508 Agenda Item 9.9

## Slide 2: Background
During RAN1#100 e-meeting, an email discussion on the reply LS to R1-2000164 was particularly revealing on the issue we may face in the future with features which are “mandatory without capability signalling”.
The topic of the LS addressed specifically the default number of antenna ports which UEs have to support for MIMO codebook type I (Single Panel)
There is a more general concern about “the introduction of signalling whose flexibility can override mandatory features without capability signalling”.

## Slide 3: Issue: mandatory features without capability signalling
Currently such features are only captured as “agreements” in TR, not in TS
Nokia has made a proposal (R1-1903151 - On features mandatory without capability, Nokia, Nokia Shanghai Bell) to copy all the mandatory features within TR38.822 into the respective sections of the other RAN2/RAN1 Technical Specifications (e.g., TS38.306, TS 38.214…)

## Slide 4: Proposal
On mandatory features without capability signalling, RAN plenary asks RAN2 to consider followings.
  The UE features which are mandatory without capability signalling as captured in TR 38.822 are captured in TS 38.306 for Rel-15, including feature group 2-32
    TS 38.306 specifies that the capability reporting by a UE cannot be in contradiction with the minimum capability defined for mandatory features without signaling
  A shadow CR is provided at the same time for Rel-16
  Note that this task shall not impact the timeline completion of Rel-16 ASN.1