## Slide 1: View on Further Enhancements on MIMO for NR
Samsung
3GPP TSG-RAN Meeting # 88e
Electronic Meeting, June 29 –July 3, 2020
Agenda: 9.10.1
RP-200619

## Slide 2: Multi-beam

## Slide 3: Background
Release 17 WI: Enhancement on multi-beam operation, mainly targeting FR2 while also applicable to FR1:
  Identify and specify features to facilitate more efficient (lower latency and overhead) DL/UL beam management to support higher intra- and L1/L2-centric inter-cell mobility and/or a larger number of configured TCI states:
    Common beam for data and control transmission/reception for DL and UL, especially for intra-band CA
    Unified TCI framework for DL and UL beam indication
    Enhancement on signaling mechanisms for the above features to improve latency and efficiency with more usage of dynamic control signaling (as opposed to RRC)
  Identify and specify features to facilitate UL beam selection for UEs equipped with multiple panels, considering UL coverage loss mitigation due to MPE, based on UL beam indication with the unified TCI framework for UL fast panel selection
Relevant deployment scenarios for FR2 (near future):
  Vehicular speed up to 80mph, US highways
  HST up to 160mph, RRHs mounted on tunnel ceiling, CPEs inside the trains
   High mobility + larger # configured TCI states (monitoring of “TX beams”)
Other potential applications:
  Industrial IOT >60 GHz
  NTN with FDD, FR2 DL FR1 UL
   At least very larger # configured TCI states
Relevant UE devices:
  Typical mobile devices
  CPEs capable of supporting up to 3 (even 4) panels @FR2  high capability UEs

## Slide 4: Targeted scenarios for Rel.17 eBM
L1-based beam indication (TCI update) to enable common DL data-control TX beam operation
  TCI state for UE-specific DCI carrying DL assignment (on PDCCH) and the DL data (in PDSCH) is common and updated together via L1 DL control channel
  Include PCI (physical cell ID) in TCI state (explicit or implicit) to facilitate L1-centric inter-cell mobility
Unified TCI framework for DL TX/UL TX beams
  Beam correspondence
  Enable common TCI state update for DL and UL
  Pooling of DL and UL measurement RS resources (CSI-RS, SSB, SRS) for source RS
  Fast panel UE switching with MPE mitigation in mind
Common framework for CSI and beam management
  CSI is rightfully complex, but BM should not be
  Forcing a common framework for CSI and BM results in cumbersome multi-beam operation
Beam management framework
  Beam indication: Different framework for UL and DL
    TCI-state framework for downlink beam indication
    Spatial Relation Information/SRS Resource Indicator framework for uplink beam indication
  Beam failure detection and beam recovery
    Target of BM should be to reduce beam failures and the need for beam recovery
  DL/UL beam indication
    Separate beam indication and beam update mechanisms for data and control via PDCCH (L1) – leading to complex “default” beam behavior
    Common indication only via MAC CE (L2)
  Separate beam indication and beam update mechanisms for uplink and downlink.
    Designed prior to RAN4 decision on beam correspondence
Efficiency and overhead issues with Rel.15/16 BM
Rel.17 direction for further enhancement

## Slide 5: Multi-TRP

## Slide 6: Background
2. Enhancement on the support for multi-TRP deployment, targeting both FR1 and FR2:
  a. Identify and specify features to improve reliability and robustness for channels other than PDSCH (that is, PDCCH, PUSCH, and PUCCH) using multi-TRP and/or multi-panel, with Rel.16 reliability features as the baseline
  b. Identify and specify QCL/TCI-related enhancements to enable inter-cell multi-TRP operations, assuming multi-DCI based multi-PDSCH reception
  c. Evaluate and, if needed, specify beam-management-related enhancements for simultaneous multi-TRP transmission with multi-panel reception
  d. Enhancement to support HST-SFN deployment scenario:
    Identify and specify solution(s) on QCL assumption for DMRS, e.g. multiple QCL assumptions for the same DMRS port(s), targeting DL-only transmission
    Evaluate and, if the benefit over Rel.16 HST enhancement baseline is demonstrated, specify QCL/QCL-like relation (including applicable type(s) and the associated requirement) between DL and UL signal by reusing the unified TCI framework

## Slide 7: Multi-TRP – PDCCH repetition (2a)
PDCCH design in Rel-15/-16
  Support of beam sweeping for P-RNTI (beam sweeping per monitoring occasion)
  In other cases, single beam per CORESET
    Can’t change beam in time domain w/o explicit signaling  hurdle for TDM repetition
Possible enhancements in Rel-17
  Enabling beam sweeping in time domain shall be the starting point.
    Beam per-CORESET  beam per SS, or beam per monitoring occasion
TCI state ID list
CORESET #A
Search space #A
Time
Beam #A
Beam #B
Beam #C
Example: multi-beam (beam cycling) per search space

## Slide 8: Multi-TRP – PUCCH/PUSCH repetition (2a)
PUCCH/PUSCH repetition in Rel-16
  Repeated PUCCH / PUSCH are allocated with the same number of RBs, across slots/sub-slots
  Such RB allocation is not optimal for multi-TRP case
    Each TRP may experience different pathloss and blockage
Possible enhancements in Rel-17
  PUCCH/PUSCH to enable flexible RB allocation per TRP
    PUCCH: Use of multiple PUCCH resources for UCI repetition
    PUSCH: Multi-DCI based PUSCH repetition
Narrow BW (to compensate large pathloss)
UE with Pc,max=23dBm
Wide BW (to compensate
small pathloss)
TRP 1
TRP 2

## Slide 9: Multi-TRP – Inter-Cell Multi-TRP (2b)
Shortcomings in Rel-15/-16
  No support for QCL reference from other cell(s) in the same frequency layer without CA-like approach
Cell #1 @CC#1
(SCI#1, PCI #1)
Cell #1 @CC#1
(SCI#1, PCI #1)
Case #1: Intra-cell Multi-TRP (MTRP)
No issue but MTRP should be done within a single cell configuration
(low flexibility)
SCI  ServCellIndex
PCI  PhysCellID
Cell #1 @CC#1
(SCI#1, PCI #1)
Cell #2 @CC#1
(no SCI, PCI #2)
Case #2: MTRP with different PCI on the same CC (non-CA framework)
Main issue: QCL reference from TRP #2 (cell #2) is not supported
(although SSB of other cell can be monitored for mobility)
Cell #1 @CC#1
(SCI#1, PCI #1)
Cell #2 @CC#1
(SCI#2, PCI #2)
Case #3: MTRP with different PCI on the same CC (CA framework)
MTRP consumes a part of CA capabilities (large RRC overhead)
Cell #1 @CC#1
(PCI #1)
Cell #2 @CC#2
(PCI #2)
Freq. domain
Spatial domain
Case #4: Conventional CA (ref.)

## Slide 10: Multi-TRP – Beam Management Enhancements (2c)
Shortcomings in Rel-15/-16
  PCell/SCell BFR triggered when all of UE-selected BFD RSs are in low quality.
    gNB may not know which BFD RS (or TRP) suffers from deep fading.
    Additional overhead required for L1-RSRP reporting
  Simultaneous Tx/Rx assuming single QCL-TypeD except PDSCH reception
Possible enhancements in Rel-17
  Partial BFR for multi-TRP
    Perform BFR partially based on new BFD RS set (e.g. per TRP)
    Fast beam change for failed TRP based on connected TRP
  Simultaneous Tx/Rx enhancements for Rx multi-panel
  Enhancements on group based beam reporting
TRP 2
TRP 1
BFR cannot be triggered
TRP 2
TRP 1
can perform
partial BFR
Rel.15/16 BFR
Rel.17 BFR (enhanced)

## Slide 11: Multi-TRP – HST-SFN Enhancements (2d)
Rel-15/-16 based transmission
  Full-SFN
    Both TRS and PDSCH are SFNed spec-transparently.
    Cons: Additional UE processing to determine whether the PDSCH is SFNed or not Additional TRS to support non-SFNed PDSCH
Enhancements in Rel-17
  SFN with multiple QCL assumption
    UE is informed whether PDSCH is SFNed or not
    No need of additional TRS for non-SFNed PDSCH
  gNB Doppler pre-compensation reusing the unified TCI state between DL and UL
  Deployment scenario: both FR1 and FR2
Figure B.3A-1: Deployment of HST-SFN (in TS 36.101)
Figure 6.1.5-2: 30 GHz deployment (in TR 38.913)
FR1: Rel-16 RAN4 HST as a starting point
FR2: uni-/bi-directional beam per RRH

## Slide 12: SRS

## Slide 13: Background
3. Enhancement on SRS, targeting both FR1 and FR2:
  a. Identify and specify enhancements on aperiodic SRS triggering to facilitate more flexible triggering and/or DCI overhead/usage reduction
  b. Specify SRS switching for up to 8 antennas (e.g., xTyR, x = {1, 2, 4} and y = {6, 8})
  c. Evaluate and, if needed, specify the following mechanism(s) to enhance SRS capacity and/or coverage: SRS time bundling, increased SRS repetition, partial sounding across frequency

## Slide 14: SRS enhancements
  Aperiodic SRS triggering
  Background
    Aperiodic SRS triggering in Rel-15: RRC configuration for codepoint to SRS resource set(s)+ DCI triggering (2bit in DCI 0_1, 1_1, 2_3 (group-based))
    Aperiodic SRS triggering enhancement in Rel-16: MAC CE based ‘aperiodic’ re-configuration of ‘spatialRelationInfo’
    Apply more flexible triggering in Rel-17
  Possible options on aperiodic SRS triggering in Rel-17
    Option 1: dynamic triggering offset control (e.g., DCI) – flexible control of slot offset via DCI
    Option 2: Automatic delaying of SRS transmission (similar as LTE)
    Option 3: Group-common DCI for SRS triggering for PDCCH overhead reduction
Antenna switching for up to 8
  Background
    Rel-15: antenna switching support for up to y = 4 antennas (UE reports a single pair of xTyR)
    Rel-16 TEI: UE can report a combination of possible pairs of xTyR
  Possible enhancements in Rel-17
    Considering possible implementations, specify SRS resource set and SRS resource(s) per set for SRS switching for up to 8 antennas (e.g., xTyR, x = {1, 2, 4} and y = {6, 8})
    Support both FR1 and FR2
  SRS capacity/coverage enhancements
  Background
    Rel-15: SRS OFDM symbols within the last 6 OFDM symbols in a slot. SRS repetition up to across 4 OFDM symbols
    Rel-16: Any OFDM symbol in a slot can be configured for SRS (from NR-U)
  Possible options
    Option 1: Bundling (e.g., time and/or frequency-domain bundling size)
    Option 2: partial sounding (e.g., definition of partial sounding)
      Interpolation/extrapolation at the gNB based on partial sounding
    Option 3: Increase repetition

## Slide 15: CSI

## Slide 16: NC-JT CSI Enhancements (4a)
Shortcomings in Rel-15/-16
  CSI report with ‘semi-static’ interference hypothesis
  Large configuration/report overhead for NC-JT CSI
    Separate CSI report shall be configured for NC-JT and non NC-JT case
    4 CSI reports for single potential NC-JT pair: large portion of UE capability is occupied (FG 2-35) No. of CSI report settings per BWP - {1, …, 4} for P/AP, {0, …, 4} for SP
CMR
IMR
Report #1 (non NC-JT)
TRP 1 (C1)
ICI (I1)
Report #2 (non NC-JT)
TRP 2 (C2)
ICI (I1)
Report #3 (NC-JT)
TRP 1 (C1)
ICI + interference from TRP 2 (I2)
Report #4 (NC-JT)
TRP 2 (C2)
ICI + interference from TRP 1 (I3)
Example of CSI report configuration for two TRPs
Possible enhancements in Rel-17
  Dynamic CSI reporting
    UE dynamically selects NC-JT or non-NC-JT CSI and reports the selected CSI depending on channel condition
  EVM: agreed SLS assumption for NR Rel-16 MTRP as baseline
    Target RU: Very low RU (5%, 10%) as well as 20%, 40%, 60%

## Slide 17: Reciprocity based CSI enhancement for FDD (4b)
WID description:
  Evaluate and, if needed, specify Type II port selection codebook enhancement (based on Rel.15/16 Type II port selection) where information related to angle(s) and delay(s) are estimated at the gNB based on SRS by utilizing DL/UL reciprocity of angle and delay, and the remaining DL CSI is reported by the UE, mainly targeting FDD FR1 to achieve better trade-off among UE complexity, performance and reporting overhead
Baseline scheme: R15/R16 Type II port selection codebook
Potential enhancements:
  Precoded CSI-RS: using angle(s) or/and delay(s)
  Codebook design: assuming angle/delay information is available at the gNB

## Slide 18: Reciprocity based CSI enhancement: Evaluation
Starting point: Evaluation assumptions for R16 Type II CSI
How to model system aspects such as the following?
  Impact on performance (baseline and potential enhancements) may need to be investigated
 | Issues
Estimation of “delay(s) and angle(s) related information at gNB | UL channel estimation and error modeling UL Tx power: same Tx power for all UEs, or realistic Tx power model (e.g. based on UL PC) SRS configuration Parameters (UL carrier frequency or UL-DL duplex distance, SRS BW, #symbols, comb, time-bundling and antenna switching) SRS configuration for potentially large (e.g. 10x) #users Frequency offset modeling (e.g. according to the FDD reciprocity model in 36.897)
Using the estimation information to obtain remaining DL CSI | Beamformed CSI-RS: beamforming can be same or different from R15/16 PS CB PAPR issue modeling
UL/DL reciprocity errors | Different transmit and receive RF circuitry at the gNB Different interference profile in UL and DL transmission