## Slide 1
Motivation on support of Free-to-Air mode in Rel-17 NR Multicast and Broadcast Services
3GPP TSG RAN Meeting #88e
Electronic Meeting, June 29 - July 3, 2020
Agenda item: 9.10.8
RP-200750
CBN, ABS, ABP, CATT, CUC, OPPO, Huawei, Reliance Jio, Samsung, ZTE

## Slide 2
Motivation
Free-to-Air mode was introduced in LTE eMBMS since Rel-14, and the definition of Free-to-Air mode can be found in TS 22.101:
  Free-to-Air (FTA) TV: A TV service characterised by no content encryption and being made available at no additional cost to the end user
Some spectrums are designated only to Free-to-Air services in some countries, and supporting Free-to-Air mode makes Rel-17 NR MBS applicable to such spectrums and makes 5G NR applicable to innovative services as well.
Free-to-Air services include but not limited to Free-to-Air TV and public safety applications.

## Slide 3
RAN Impact Analysis
RRC_IDLE state and RRC_INACTIVE state are supported in Rel-17 NR MBS WI [1]
  Specify RAN basic functions for broadcast/multicast for UEs in RRC_IDLE/ RRC_INACTIVE states [RAN2, RAN1]
According to LTE work in Rel-14, additional effort to support basic Free-to-Air mode on top of RRC_IDLE state can be very small
  RAN2 concluded: From RAN2 point of view there is no difference in the way the MBMS data is delivered to Receive Only Mode and legacy eMBMS UEs. [2]
  Small change on stage 2 specification enables Receive Only Mode from RAN perspective [3]
Supporting Free-to-Air mode does not mean supporting MPMT (Medium Power Medium Tower) and HPHT (High Power High Tower), and hence does not conflict with the way forward agreed in RAN#83 [4]

## Slide 4
SA Impact Analysis
SA2 study/23.757 progressed well so far focusing on NR connecting to 5GC
The broadcast service definition is included as below in 23.757 (Free-to-Air service can be treated as one of the broadcast service):
  Broadcast communication service: A communication service in which the same service and the same specific content data are provided simultaneously to all UEs in a geographical area (i.e., all UEs in the broadcast coverage area are authorized to receive the data).
Key issue #1: MBS session management includes both the broadcast and multicast service
Some solutions introduced in the TR can be used to serve the Free-to-Air MBS service as the starting point
The other impact regarding the support of Free-to-Air service needs to be discussed in SA2

## Slide 5
Proposal
Revise Rel-17 NR Multicast and Broadcast Services WID at RAN#88e to include support of Free-to-Air mode for NR
Liaison SA/SA2 about RAN decision and respectfully ask SA/SA2 to take RAN decision into consideration
No support of Free to air/receive only mode is provided in this WI.
Any design decisions taken for this WI in Release 17 shall not prevent introducing the following features in future Releases:
  Standardised support of SFN over multiple cells above gNB-DU level;
  Support of Free to air/receive only mode
Specify RAN basic functions for broadcast/multicast for UEs in RRC_IDLE/ RRC_INACTIVE states, including support of Free-to-Air mode [RAN2, RAN1]:

## Slide 6
References
[1] RP-193248, “New Work Item on NR Multicast and Broadcast Services”, Huawei , December 2019
[2] R2-165971, “Reply LS on RAN impacts of Shared MBMS Network and Receive Only Mode in eMBMS”, RAN2, August 2016
[3] R2-168956 , “Receive Only Mode for enTV”, Qualcomm, November 2016
[4] RP-190717, “Way forward on 5G Broadcast”, March 2019