## Slide 1: Motivation for SI: Study on NR Sidelink Positioning
Agenda Item: 9.1
Source: Intel Corporation
Document for: Discussion
3GPP TSG RAN Meeting #88-E RP-200898
June 29 - July 03, 2020

## Slide 2: Introduction Overview of Rel.16 NR Positioning Framework
Positioning
  One of the most popular and demanded services along with communication service
NR Release 16 Technology
  Defined solid framework to facilitate RAT dependent positioning methods
    DL-TDOA, DL-AoD, UL-TDOA, UL-AoA, multi-RTT, E-CID + hybrid positioning techniques
    Network & UE based RAT dependent positioning solutions for positioning
    Strict target performance requirements on positioning accuracy
      < 1m indoor and 3m outdoor horizontal positioning accuracy
      < 1s end-to-end latency for positioning
  Assistance for RAT independent positioning solutions for precise positioning
    Tight integration w/ sister technology - GNSS solutions for precise positioning, etc.

## Slide 3: NR Positioning Evolution in Rel.17 Enhancements of NR Positioning Study Item
Study item on enhancements of NR Positioning is started in May 2020
  Motivation - New industrial IoT use cases, scenarios and target performance
    Less than [0.2-1] m positioning accuracy
    Less than < [10-100] ms latency requirement (end-to-end)
  Potential enhancements areas
    Low latency positioning solutions and signaling protocols
    Solutions to improve accuracy of horizontal and/or vertical positioning performance
    Integrity of NR positioning solutions
  All NR positioning solutions defined so far are based on Uu air-interface design
    DL & UL reference signals and UE & gNB measurements
  Benefits of sidelink air-interface (PC5) are still not explored and not utilized by 3GPP NR

## Slide 4: NR Positioning Enhancements in Rel. 17 and Beyond Sidelink Air-Interface for NR Positioning
C-V2X use cases require support of positioning in and out of NW coverage
  Sidelink is the only NR interface that can be used for positioning in out-of-coverage scenarios together with GNSS
  Sidelink can be used to perform direct ranging b/w UEs or UEs and RSUs
Integration of sidelink opens new performance bounds for NR positioning
  More links for UE positioning reference signal transmissions and measurements
  Additional UE based reference sources with known precise time and coordinates
  Cooperative positioning principles and higher layer protocols
  Proximity based solutions and crowdsourcing
  Empowers Uu RAT dependent and RAT independent positioning solutions

## Slide 5: NR Positioning Enhancements in Rel. 17 and Beyond Sidelink Air-Interface for NR Positioning
Sources of GNSS performance degradation
  Satellite outages, atmospheric conditions, availability issues
  Satellite geometry leads to reduced accuracy
  Multipath signal propagation in indoor, urban and dense urban environments
Satellite augmentation by NR cellular network + sidelink radio interfaces

## Slide 6: Sidelink NR Positioning for V2X Use Cases Importance of NR Sidelink
  Majority of V2X applications demand and rely on accurate object positioning
  Emerging autonomous driving systems actively utilize GNSS, camera and radio-vision
    Radars/lidars measure relative distance, speed, sense on road objects and can be complemented by NR radio-vision and communication solutions
  NR sidelink radio designed for V2X use cases is expected to enter market in near future
    On top of communication service, future sidelink radio can also provide ranging/positioning
  Sidelink aided positioning is of strong interest in automotive sector [5GAA LS – R1-2003253] and its benefits should be explored through 3GPP study and evaluation
  Automotive standard organizations develop / finalize protocols to support positioning
    ETSI EN “Intelligent Transport Systems (ITS); Facilities Layer function; Part 2: Position and Time management (PoTi); Release 2”
    SAE J2945/7 “Positioning Enhancements for V2X systems”

## Slide 7: SID Objectives Sidelink for NR Positioning
RAN Study Item Objectives
  Study use cases and requirements for sidelink-aided NR positioning
    Prioritize V2X use case as a starting point for development
    Later consider extension to I-IoT, public safety, general commercial use cases
  Study deployment / operating scenarios for sidelink-aided NR positioning
    In and out of NW coverage, indoor and outdoor, 2D and 3D, dense and sparse
Proposal
  Inform SA WG about RAN WG study on sidelink positioning in order to analyze potential impact on positioning architecture and other higher layer protocols