## Slide 1
Views on the objectives for unlicensed band URLLC/IIoT operation
3GPP TSG-RAN WG Meeting #88-e
e-Meeting, June 29th – July 3rd, 2020
RP-200947

## Slide 2
Controlled environment
  According to the WID RP-193233, “controlled environments” is assumed to be an environment installed by the facility owner and where only sporadic interference happens.
It is necessary to have a common understanding for the “controlled environments” since it has impacts on the scope of potential enhancements for unlicensed band URLLC/IIoT. Followings need to be clarified:
  Single operator vs. Multiple operators?
  Wi-Fi absence vs. Wi-Fi presence?
  Target LBT scheme for the controlled environment?
  LBT failure probability?
To meet the QoS requirement of URLLC/IIoT services on unlicensed band,
  At least support the controlled environment where the URLLC/IIoT services is operated by a single operator in a network without co-existence with Wi-Fi.
  At least support FBE scheme to meet the regulation requirements for unlicensed band.
  Whether to increase the transmission opportunities in frequency and/or time domain depends on the assumption of LBT failure probability

## Slide 3
Enhancements of R16 IIOT/URLLC featured in NR-U (1)
  At least support following enhancements as objectives to ensure Release 16 feature compatibility with unlicensed band URLLC/IIoT operation
  Enhanced functionalities for DCI format 0_2/1_2
  Enhanced HARQ-ACK codebook(s) with different priorities
    Support enhanced type 2 codebook with different (High and low) priorities
    Support enhanced type 3 HARQ-ACK codebook containing high and/or low priority HARQ-ACK feedback for PDSCHs
DCI format 0_2 | DCI format 1_2
Support CG-DFI indication for configured grant Support of interlaced UL resource allocation Support of multi-PUSCH scheduling Enhanced DAI for enhanced type 2 HARQ-ACK codebook ChannelAccess-CPext-CAPC Support of Scell dormancy indication (case 1) | One-shot HARQ-ACK request for type 3 codebook Support enhanced type 2 codebook, including PDSCH group index New feedback indicator Number of requested PDSCH group(s) ChannelAccess-Cpext Support of Scell dormancy indication (case 1 and case 2)

## Slide 4
Enhancements of R16 IIOT/URLLC featured in NR-U (2)
  At least support following enhancements as objectives to ensure Release 16 feature compatibility with unlicensed band URLLC/IIoT operation
    Enhanced PUSCH
      Support of multi-PUSCH transmission (DG and CG) with type A or type B repetition for each PUSCH transmission
    Enhanced DL SPS
      HARQ-ACK feedback skipping for DL SPS if the SPS is not tranmistted by the gNB due to LBT failure
      For enhanced type 2 HARQ codebook, HARQ-ACK retransmission for DL SPS due to LBT failure
    Enhanced Intra-UE UCI multiplexing to reduce UCI dropping considering the LBT in NRU
      Parallel PUCCH and PUSCH transmissions at least on different CCs,
        i.e., PUCCH on licensed CC and PUSCH on unlicensed CC.
      UCI multiplexing on PUSCH depends on the LBT category and/or LBT outcome of the PUSCH

## Slide 5
NR-U enhancements to support URLLC/IIOT
  Support FBE as channel access mode for URLLC/IIOT unlicensed band operation and support following enhancements:
      Support of UE initiated COT for UL transmission (DG and CG) in FBE mode, including the ED threshold determination
      Consider different FFPs for gNB and UE, and different FFPs for different services.
      Consider service dependent ED threshold
  Support of UL wideband transmission alt 2, i.e. UE transmits PUSCH (DG and CG) on all sub-bands within the sub-block of scheduled/configured PUSCH which passes CCA
  Support 2-step RACH with no gap between MsgA PRACH and MsgA PUSCH, MsgA PRACH and MsgA PUSCH transmission in the same slot

## Slide 6
Objectives in Approved WI of RP-193233
Study, identify and specify if needed, required Physical Layer feedback enhancements for meeting URLLC requirements covering UE feedback enhancements for HARQ-ACK [RAN1] CSI feedback enhancements to allow for more accurate MCS selection [RAN1] Note: DMRS-based CSI feedback is not in scope of this WI Identify potential enhancements to ensure Release 16 feature compatibility with unlicensed band URLLC/IIoT operation in controlled environment [RAN1, RAN2] Detailed objectives to be clarified at RAN#87 based on essential issues to be identified in RAN#87 (if any) Intra-UE multiplexing and prioritization of traffic with different priority based on work done in Rel.16 [RAN1]: Specify multiplexing behavior among HARQ-ACK/SR/CSI and PUSCH for traffic with different priorities, including the cases with UCI on PUCCH and UCI on PUSCH. Enhancements for support of time synchronization: RAN impacts of SA2 work on uplink time synchronization for TSN, if any. [RAN2] Propagation delay compensation enhancements (including mobility issues, if any). [RAN2, RAN1, RAN3, RAN4] RAN enhancements based on new QoS related parameters if any, e.g. survival time, decided from SA2. [RAN2, RAN3]