## Slide 1: RAN schedule for the Multi-SIM WI
vivo, Charter Communications, China Telecom, Verizon, Intel
3GPP TSG RAN#88e June 29 - July 3, 2020 E-meeting | TDoc RP-200951 Agenda Item 9.10.12

## Slide 2: Background
SA2 solutions assume RAN impact (UE, NG-RAN)
 | SA2 Solution highlight（TR23.761） | Potential impacts | Related to RAN2 MSIM WI objective X
Key Issue 1: Handling of Mobile Terminated service with MSIM device | Paging Cause in the Uu Paging message (Sol 1) | RAN2/3 | Obj 3 on Paging Cause
 | Negotiated “absence” (Sol 2) | RAN2/3 | 
 | RRC Busy indication as a response to Uu Paging (Sol 3) | RAN2/3 | 
 | Network-based paging filtering (Note 1) | RAN2/3 | Obj 3 on Paging Cause
Key Issue 2: Enabling Paging Reception for MSIM Device | UE negotiates “scheduling gap” in RAN A to listen paging in RAN B (Note 1) | RAN2 | on paging purposes
 | Implementation-based (e.g. alternating USIMs when monitoring POs) (Note 1) | RAN2 | Obj 1 on paging collision
Key Issue 3: Coordinated leaving for MSIM device | Local RRC release in NG-RAN based on N2 request. (Sol 4) | RAN2/3 | Obj 2 on Leaving Message
 | UE-requested Leave/resume via RRC (Sol 5/6) | RAN2/3 | Obj 2 on Leaving Message
Note 1: New agreed solutions to be captured in TR 23.761

## Slide 3: Motivation to start at Q3
According to the current SA2 work plan, the FS_MUSIM study and normative work are scheduled for completion in Q3 and Q4
Majority of proposed solutions by SA2 require RAN WGs evaluation and input to allow SA2 to conclude the SI as scheduled and down select the right solutions for normative works.
Observation: early RAN2 analysis about both RAN2 and SA2 related solutions will help SA2 progress and SA2 SI completion.
Proposal: RAN2 MSIM WI should begin at RAN2 2020 Q3 meeting

## Slide 4: Annex: Potential RAN2 MSIM Time Plan
 | Obj1:Paging Collision | Obj2: Coordinated Leaving | Obj3: Paging Cause
2020Q3 | Potential solutions description | Scenarios for UE leaving Message Evaluation of SA2 MUSIM SI solutions | 
2020Q4 | Solution evaluation and down selection | Solutions for UE leaving message for identified scenarios | 
2021Q1 | Solution specification, if needed, for paging solutions | Solutions for UE leaving message for identified scenarios Stage 2 description | Initial discussion on paging cause based on SA2 progress
2021Q2 | Finalizing solutions and stage 3 description | Continue stage 2 and begin stage 3 Solutions for UE leaving message for identified scenarios | Detailed solutions
2021Q3 | Stage 2 corrections, Finalizing stage 3, WI completion |  |