## Slide 1: On efficient usage of operator spectrum that is not aligned with NR channel bandwidths
T-Mobile USA
3GPP TSG-RAN Meeting #88-e RP-201130
Online, , June 29 – July 3, 2020

## Slide 2: Operator requests for new channel bandwidths
Band | Channel Bandwidth
n5 | 7, 11 MHz
n12 | 12 MHz
n3, n8, n25, n66, n71 | 35 MHz
n3, n25, n66 | 45 MHz
n26 | 3, 7 MHz
n28 | 13, 33 MHz
A poll on the RAN4 and RAN reflectors produced requests for new channel bandwidths shown in this table
Operators aren’t exactly requesting every channel bandwidth from 1 to 100 MHz as some had feared
Note: 35 MHz was initially included in the WID for wider channel BWs for n25, but is being removed from the WID after discussions in RAN4.

## Slide 3: Alternatives to creating new channel bandwidths
Use the next wider channel BW
with only a subset of the RBs
40 MHz channel BW
35 MHz license
Usable RBs
Intra-band CA
35 MHz license
X MHz CC
Overlapping UE channel BWs
35-X MHz CC
35 MHz license (and BS CH BW)
30 MHz UE CH BW
30 MHz UE CH BW

## Slide 4: Using the next wider channel BW with only a subset of the RBs
The idea that has been proposed is that an operator would use a channel BW that is wider than its licensed BW, and only use a subset of the RBs [1].
One problem with this approach is that 3GPP emission requirements are based on the channel BW, not the allocated RBs. Therefore the emissions requirements would be based on the wider channel BW and not the narrower operator’s licensed BW, so there is no guarantee that regulatory emission requirements like SEM would be met.
On the receiver side, there would be a blocking issue due to neighbor emissions if a channel BW is used that is wider than the operators spectrum license.
Observation 1: The use of the next wider channel BW with a subset of RBs will not be acceptable to operators and regulators because 3GPP emissions requirements would be based on the wider channel BW and not on the operator’s licensed bandwidth, and receiver blocking will be problematic.
Use the next wider channel BW
with only a subset of the RBs
40 MHz channel BW
35 MHz license
Usable RBs

## Slide 5: Example of using the next wider channel BW with only a subset of the RBs (centered)
Example with 35 MHz of RBs centered in a 40 MHz carrier
UE SEM would be based on the 40 MHz channel, but the regulatory emission requirements would be based on the 35 MHz licensed BW

## Slide 6: Example of using the next wider channel BW with only a subset of the RBs (at the band edge)
Example with 35 MHz of RBs aligned with a 40 MHz channel at the low end of the band
The top end of the channel would be offset by 5 MHz from the top of the 35 MHz license
UE SEM would be based on the 40 MHz channel, but the regulatory emission requirements would be based on the 35 MHz licensed BW

## Slide 7: Using the next wider channel BW with only a subset of the RBs (Downlink)
On the downlink, if 35 MHz of RBs were used with a 40 MHz channel BW aligned with the edge of the band, the UE receiver would be subject to blocking from the operator in the adjacent spectrum.
Also on the DL, if the BS used 40 MHz instead of 35 MHz, it would likely interfere with the neighbor’s spectrum as well.
35 MHz operator license
40 MHz carrier
Potential blocker

## Slide 8: Use of intra-band CA
Another suggestion to efficiently cover operators’ licensed spectrum is to use intra-band CA to cover bandwidths like 35 MHz or 45 MHz.
Intra-band CA to cover 35 MHz could require a bandwidth combination set of 30+5, 25+10, 20+15, 15+20, 10+25 and 5+35. So, is it really much better for the UE to have to implement and test all of these bandwidth combinations, or just a new channel BW of 35 MHz?
Intra-band CA will be slightly less spectrally efficient than a wider channel BW.
Observation 2: Intra-band CA would avoid the complexity of adding new channel BWs but would add complexity for supporting intra-band CA.
Intra-band CA
35 MHz license
X MHz CC
35-X MHz CC

## Slide 9: Overlapping UE channel Bandwidths
In some cases it may be possible to use two UE channel bandwidths that are smaller than the UE channel bandwidth to cover the operator’s licensed spectrum.
While each individual UE cannot use the entire licensed bandwidth, the network could use the entire bandwidth.
New gNB channel BWs would be needed.
For overlapping channels, both channels need to cover the SSB.
A modification of this approach would be to use existing overlapped BWPs for the uplink, and define a new 35 MHz channel BW for the downlink.
Overlapping UE channel BWs
35 MHz license (and BS CH BW)
30 MHz UE CH BW
30 MHz UE CH BW

## Slide 10: Proposals
Option 1:
  Proposal 1a: 35 and 45 MHz have been requested by several operators for multiple bands. RAN should approve a WI for 35 and 45 MHz
  Proposal 1b: 7 MHz cannot efficiently be covered by intra-band NR CA or overlapping channels because two separate SSBs would be required, doubling the overhead. RAN should approved a WI with 7 MHz for n26 or add 7 MHz to the n26 WI.
  Proposal 1c: RAN Plenary should approve a study item on the approaches for efficient utilization of operators’ spectrum that does not align with NR channel bandwidths for channel bandwidths other than 35, 45 and 7 MHz.
Option 2:
  Proposal 2a: RAN Plenary should approve a study item on the approaches for efficient utilization of operators’ spectrum that does not align with NR channel bandwidths.

## Slide 11: References
[1] R4-1911519, “Views on adding new Channel Bandwidths for NR bands,” Apple