## Slide 1: Motivation for WID: Introduction of DL 1024QAM for NR FR1
Ericsson
3GPP TSG-RAN Meeting #88
Electronic Meeting, June 29-July 03, 2020
Agenda item: 9.1.2
RP-201155

## Slide 2: Motivation
Rel-15 NR supports downlink modulation order up to 256QAM for PDSCH.
LTE has introduced even higher order modulation order of 1024QAM for PDSCH in Rel-15.
NR should be competitive to LTE with regard to the spectral efficiency especially on refarmed operating bands and mid-bands, i.e., FR1
Even for NR, high SNR conditions supporting DL 1024QAM can be achievable in FR1 with:
  Small cell / indoor cell / non-sectorized cells
  Beamforming (in mid-bands 3-6 GHz)
It is expected that meeting EVM and demodulation requirements in the FR1 range should be similar to those for LTE from an implementation perspective and feasible.

## Slide 3: Summary of core WI objectives
Specify downlink 1024QAM for NR PDSCH operation in FR1:
  Specify high order modulation for PDSCH [RAN1]
    Specify 1024QAM constellation as specified in E-UTRA for DL PDSCH
    Specify corresponding MCS table
    Specify corresponding CQI feedback
  Specify corresponding RRC signalling and UE capabilities [RAN2]
  Specify corresponding RF requirements [RAN4]

## Slide 4: Summary of performance WI objectives
Specify UE performance requirements for DL 1024QAM for PDSCH in FR1 [RAN4]
  UE demodulation performance requirements for PDSCH
  CQI reporting requirements